29 October 2012

Number 7184

Improved Power, Stability And Control For New 8 WX Series

Case Construction Equipment has unveiled the first three models in an improved range of wheeled excavators. The WX148, WX168 and WX188 benefit from the power and performance of a three-pump hydraulic system, with a dedicated swing pump, a new engine speed/working mode selection dial, a heavy-duty undercarriage and an improved operator’s cab. The revisions result in improved operator comfort and ease of operation, excellent service accessibility and reduced ownership costs.

Power And Control

The Case wheeled excavators use a three-pump hydraulic system, with one pump dedicated to the slew function. This provides continuous movement and allows the operator to multi-function the controls for smooth, productive digging performance. The extra powerful hydraulics are managed by the Case Intelligent Hydraulic System control, which offers a single CPU for improved controllability and simplified diagnostics.

Automatic Powerboost is included on all three models, to deliver optimum performance for heavy breakout and lifting operations. There is also an automatic power increase in travel mode to ensure rapid travel between working areas. Improved orbitrol steering provides easy to use, effortless steering performance.

A new engine speed and new working mode selection dial provides a single point of contact for the operator when setting the machine to work. This dial delivers low idle speed, Lift 1 and 2 modes for dedicated lifting work, Eco working modes 1, 2 and 3, plus a Heavy Mode for maximum excavating performance. There is also a dedicated road travel mode for rapid relocation between sites.

Case Intelligent Swing (CIS) allows the operator to adjust upper structure slew speed to suit a variety of work sites. The machines offer four swing acceleration settings and three deceleration settings, adding to the wheeled excavators’ versatility and making the machines easier to operate in confined urban situations.

Stable Working Platform

Case excavators have a reputation for robust design and strong build, established over many years of reliable service. The latest WX models have an extremely robust chassis with the option of a dozer blade, a dozer blade and stabilisers, or stabilisers front and rear, for total balance and a solid working platform.

The machines drive through a new fully automatic hydrostatic powershift transmission that is directly mounted to the rear axle for maximum ground clearance. With new heavy duty ZF axles, the excavators deliver high travel speeds up to 35km/h, yet also provide total control on site through a creep speed function.

The robust axle design offers excellent drawbar pull and the axles feature an auto locking system for maximum stability when working without stabilisers. Multi-disc wet brakes and axle oil change intervals of 2,000 hours deliver reduced operating costs and reassuringly powerful braking from full speed. Customers can choose single tyres, twin tyres or super wide tyres for maximum flotation off-road.

Improved Comfort And Control

The ROPS/FOPS operator’s cab on the WX machines fully meets all EU regulations, delivering a comfortable and safe working environment. With automatic air conditioning, and air-suspended seat and completely adjustable controls, all operators will be able to find a comfortable working position, reducing fatigue and increasing productivity.

The viscous mounted and noise insulated cabin has ergonomically designed arm rests and foot pedals, with tinted safety glazing and large sun blinds, for maximum visibility all round. All travel functions have been centralised on the steering column, with other switchgear grouped for ease of reach. A new LCD multifunction monitor provides information for the operator and integrated diagnostic functions for service engineers.

The three-pump hydraulic system allows the operator to use multiple excavator functions, for continuous movement while digging and grading. This makes the machines easier to operate, reducing fatigue and increasing productivity for the customer.

Reduced Operating Costs

All three excavators had new long life bushings as part of their robust boom and arm design. These provide 500 hour greasing intervals for the WX168 and WX188 and 100 hour intervals for the WX148. Safety valves are standard on the main boom, and Case offers a handling kit including dipper arm safety valves, loading hook or eye and an overload warning system as an option.

Wide opening service access doors provide excellent ground level serviceability, with remote mounted oil and fuel filters along with remote grouping for grease points. A refuelling pump is easily reached from ground level and the machines have side by side radiators for maximum cooling efficiency. There is a removable net protecting the radiators, making it easier to clean the cooling pack in dusty conditions.

Quick Specifications

WX148

Operating weight: 15.2-16 tonnes

Engine: Four cylinder 90kW Tier 3

Bucket size: to 0.73m3

Max travel speed: 35km/h

Bucket digging force: 99.5kN

Arm digging force: 72.9kN

WX168

Operating weight: 17-17.9 tonnes

Engine: Six cylinder 105kW Tier 3

Bucket size: to 1m3

Max travel speed: 35km/h

Bucket digging force: 112kN

Arm digging force: 73.8kN

WX188

Operating weight: 18.2-19.7 tonnes

Engine: Six cylinder 118kW Tier 3

Bucket size: to 1m3

Max travel speed: 35km/h

Bucket digging force: 136kN

Arm digging force: 91kN

Visiting our website, you will be able to download texts, high resolution image files and videos related to this press release (jpg 300 dpi, CMYK): www.casecetools.com/press-kit

Case Construction Equipment sells and supports a full line of construction equipment around the world, including the No. 1 loader/backhoes, articulated trucks, crawler and wheeled excavators (including compact), telescopic handlers, motor graders, wheel loaders (including compact), vibratory compaction rollers, crawler dozers, skid steers, compact track loaders, tractor loaders and rough-terrain forklifts. Through Case dealers, customers have access to a true professional partner—with world-class equipment and aftermarket support, industry-leading warranties and flexible financing. More information is available at www.casece.com.

Case is a division of CNH Global N.V., whose stock is listed at the New York Stock Exchange (NYSE:CNH), which is a majority-owned subsidiary of Fiat Industrial S.p.A. (FI.MI). More information about CNH can be found online at www.cnh.com .

# # #

PRESS CONTACTS

Released by:

TLC PR for ALARCON & HARRIS

Lynn Campbell

Tel: +44 151 227 4957

E-mail: lynn@tlcpr.co.uk