25 february 2016

New Holland series TT4: redefining the economy tractor benchmark

- Efficient and productive turbocharged FPT Industrial engines

- Tailored transmission offering a Synchronised Shuttle and creeper option

- 54  litres per minute hydraulic flow

- Segment-leading operator comfort thanks to a large flat deck platform with suspended pedals, designed to provide maximum operator comfort with spacious leg room and easy entry/exit.

- Standard with Foldable ROPS and canopy

New Holland’s new TT4 economy utility tractor range is set to redefine the economy tractor market in this ever expanding segment. The new TT4 introduces more productivity boosting features in a complete package that delivers reliability, simplicity, and low cost of ownership, at a very economical price.

This range of tractors offers four models: the TT4.55, TT4.75 and TT4 80 and TT4 90, producing engine powers from 55 to 88 hp. TT4.80 and TT4.90 models are the new released ones and will be the focus of AME area.

The TT4 is set to replace the original Series TD which revolutionised the economy tractor market. The New Holland Series TD tractor delivered proven technology reliability, simplicity, and low cost of ownership, at a very economical price.

The new line up enhances the choice available to farmers, small holders, local government / municipalities and other operators who are looking for a highly versatile tractor. It offers excellent manoeuvrability, ergonomic comfort and fuel efficiency. The complete range is ideally suited to a wide range of both agricultural and non-agricultural tasks, including front loader activities, hauling and PTO work. The entire TT4 series benefits from New Holland’s acclaimed ergonomic excellence and distinctive styling cues.

Economical engines for precision performance

FPT Industrial’s S8000 turbocharged mechanical fuel injection engine TT4 models run fuel efficient  TT4.55, TT4.75  Tier 3 with 3 Cylinder 2,9L Engine, TT4.75 Tier 1 with 4 Cylinder 3.9L Engine, TT4.80, TT4.90 Tier3 with 4 Cylinder 3.9L Engine for dynamic performance and fuel economy. Higher hp models, utilizes  turbo charger and inter-cooler technology, meaning the engines run cleaner, deliver impressive power and torque and maintain performance even at raised altitudes. Utilizing turbo charger technology on all models, and Inter Cooler technology on the TT4.75, TT4.80 and TT4.90, the engines not only

The 2.9 litre powerplant boasts two valves per cylinder and offers maximum torque of up to 300 Nm guaranteeing outstanding productivity for the most demanding applications, The engine uses Tier 3 technology to meet engine emission standards. Overall vehicle efficiency is further enhanced with a 540 eco PTO speed. This enables the engine to run at a lower working speed for reduced fuel consumption. Add to that 300 hour service intervals and the TT4 delivers plenty of power with economical running costs.

Tailored transmission offering

A new 12 x 12 transmission offering is standard throughout the entire range and is enhanced with the addition of the dash mounted synchronised shuttle control. This dash mounted lever can be operated without removing the hand from the steering wheel, enhancing safety and improving loader productivity. An optional 20 x 20 creeper transmission is available for all models, with speeds as low as 0.27km/h (270m/hr) it’s ideally suited for specialist activities and precision applications.

The transmission controls will be familiar to users of New Holland tractors: situated either side of the operator, all gear changes can be carried out from the comfort of the seat, without the need to stretch and reach, and enable the operator to easily switch from the steering wheel to the lever for the ultimate in ergonomic operation and safety.

Precision hydraulics

Designed with your application in mind, the capacity of the dedicated implement pump is an impressive 54  Lpm, this ensures the required hydraulic performance even when carrying out the most demanding applications, including front loader and hay and forage applications.

Back that up with a dedicated 26 L/min for mechanical shuttle and 31 L/min for power shuttle option independent steering pump, and the result is steering accuracy that is maintained without compromising loader cycle times, or three point linkage operation

Purpose-Designed for Loader Work

New Holland AP Plus loaders have been specially developed for the New Holland TT4 tractor range. Designed for Australian conditions, and featuring excellent visibility, their durable performance and solid construction allows operators to handle bigger tasks for longer periods.

New Holland’s mechanical level lift system is the best form of operator protection against “rollback” and is designed to meet the stringent standards of the TMA Code of Practice for Supply and Manufacture of Front End Loaders. They also feature the “Cam Lock” attachment system, which secures the loader arm in place and is easily released without the use of any special tools.

Designed with service access and visibility in mind the excellent visibility to the bucket is thanks to the loaders mid-mount design, narrow boom arms and small uprights. All key pivot points are fitted with heavy-duty bushes. These can all be lubricated from the side of the loader, with easy to see recessed grease points.

New Holland AP Plus Series Loaders can be specified with a choice of Standard or 4in1 bucket designs. With integrated park stands and colour coded hydraulic couplers these loaders truly are a multipurpose tool.

ROPS platform

The new TT4 range ROPS platform has been engineered by design with specific trim, fenders and noise protection to enhance the operator’s experience. A canopy for the ROPS frame is also standard equipment.

Striking New Holland styling

The striking TT4 styling is reminiscent of the award winning T7 range. Key New Holland styling cues have been integrated into the overall design, including the distinctive front hood lights and oval front and rear work lights to guarantee impressive visibility. They have been combined with the brand’s signature sloping nose for unobstructed forward visibility.

| Model | Rated power ISO TR14396-ECE R120 @ 2300rpm [kW/hp(CV)] | Wheelbase | Weight | Max. torque @ 1400rpm (Nm) |
| --- | --- | --- | --- | --- |
| T4.55 | 41/55 | 2079 | 2286 | 213 |
| T4.75 | 55/75 | 2200 | 2514 | 306 |
| T4.80 | 59.7/80 | 2258 | 2825 | 310 |
| T4.90 | 65.7/88 | 2258 | 2825 | 340 |

New Holland Agriculture's reputation is built on the success of our customers, cash crop producers, livestock farmers, contractors, vineyards, or groundscare professionals. They can count on the widest offering of innovative products and services: a full line of equipment, from tractors to harvesting, material handling equipment, complemented by tailored financial services from a specialist in agriculture.  A highly professional global dealer network and New Holland’s commitment to excellence guarantees the ultimate customer experience for every customer. For more information on New Holland visit www.newholland.com

New Holland Agriculture is a brand of CNH Industrial N.V. (NYSE: CNHI /MI: CNHI) a global leader in the capital goods sector with established industrial experience, a wide range of products and a worldwide presence. More information about CNH Industrial can be found online at www.cnhindustrial.com

http://it.youtube.com/user/NewHollandAG

www.flickr.com/photos/newholland

http://www.facebook.com/NHAgriUKandROI

http://twitter.com/NewHollandAG

https://plus.google.com/117086178528241801087/posts

Press contacts:

Caterina Cattaneo, New Holland Agriculture. Phone: +390110086158, 
email: caterina.cattaneo@newholland.com