Press information

Volvo Trucks’ flagship celebrates with 750 hp

The Volvo FH16 is now available with 750 hp and 3550 Nm to handle the heaviest and most demanding transport assignments. It will reach the market just in time to celebrate the 16-litre engine’s 25th anniversary.

1987 saw the introduction of the Volvo F16 with Volvo’s first-ever 16-litre engine, producing 470 hp. Since then, market needs have driven the development towards increasingly powerful trucks.

“With the Volvo FH16 750 we can offer our customers a truck with absolute top performance, good fuel efficiency and extremely low emissions. It’s an uncompromising combination for the heaviest and most demanding of transport operations,” says Staffan Jufors, President and CEO of Volvo Trucks.

Performance, fuel efficiency and environment

The new engine is based on the same technology as Volvo Trucks’ current 16-litre 700 hp diesel engine – an in-line six with overhead camshaft, four valves per cylinder and unit injectors. It has been optimised for higher power and torque but fuel consumption is unchanged. The 750 engine is available in two versions, one for Euro 5 and the other for EEV (Enhanced Environmentally-friendly Vehicle), giving even lower particle emissions and less smoke.

The Volvo I-Shift automated gearchanging system is fitted as standard and has been modified to handle the engine’s high torque. The rear axle range encompasses axles for gross combination weights of up to 250 tonnes. For fast long-haul duties, the recently introduced RS1360 solo axle is a fuel-efficient alternative.

Driveability and productivity

The new 750 engine produces 2800 Nm of torque at 900 revs/minute, after which the torque curve rises sharply and reaches its peak level of 3550 Nm at 1050 revs/minute, then levels out to 1400 revs/minute. This makes it possible to maintain a high speed on even the toughest uphill climbs.

“The more power you have at your disposal at low revs when starting to haul a heavy load, the less strain on the engine and the more fuel-efficient your progress. This in turn results in superb drivability,” says Hayder Wokil, product manager at Volvo Trucks.

The Volvo FH16 750 is intended both for truly heavy transport duties and for assignments that demand high average speed running on hilly or very hilly roads.

“For most FH16 customers, the focus is on transporting as many tonnes as possible in the shortest possible time. However, many customers also need to quickly transport high-value goods and fresh products across long distances with varying topography and deliver just-in-time,” explains Wokil.

Heavier transports – more powerful trucks

There has long been a trend towards increasingly heavy transports and thus also a greater need for more powerful trucks. Since the introduction of the Volvo F16 in 1987 and the first-generation 16-litre engine producing 470 hp, power levels have risen step by step in pace with market and customer needs. In 1993 power rose to 520 hp. Ten years later an all-new engine arrived, producing 610 hp. In 2009 Volvo was the first manufacturer to reach 700 hp, and now it is time for the next step – the Volvo FH16 750 hp.

Production of the first Volvo FH16 trucks for the European market with the higher power output will get under way in the beginning of 2012. In addition to the 750 hp version, Volvo’s 16-litre engine is available with power outputs of 540, 600 and 700 hp.

Link to a film about the new FH16 750: http://volvo.qbrick.com/index.aspx?cid=2&mode=3&mid=763

Link to running footage: http://volvo.qbrick.com/index.aspx?cid=2&mode=3&mid=751

September 8, 2011

For further information, please contact:

Per Nilsson, Media Relations Europe, phone +46 31 323 3349,

e-mail per.nilsson.pr@volvo.com

Visit http://www.thenewsmarket.com/volvogroup to access broadcast-standard video about the Volvo Group’s various production plants and products. You can download graphic images in the form of MPEG2 files or order them on Beta SP tape. Registration and video are free to the media.

Images are available in the Volvo Trucks image bank http://imagegallery.vtc.volvo.se/.

Volvo Trucks provides complete transport solutions for professional and demanding customers. The company offers a full range of medium to heavy duty trucks. Customer support is secured via a global network of 2,300 dealers and workshops in more than 140 countries. Volvo trucks are assembled in 16 countries across the globe. In 2010 more than 75,000 Volvo trucks were delivered worldwide. Volvo Trucks is part of the Volvo Group, one of the world’s leading manufacturers of trucks, buses and construction equipment, drive systems for marine and industrial applications, aerospace components and services. The Group also provides solutions for financing and service.