Press information

THE NEW VOLVO FH SERIES: SAFETY

# “The safest Volvo in the world”

The driver of a new Volvo FH would emerge from an 80 km/h collision without any serious injuries. And if the truck rolled over, there is an emergency exit at hand.
But not only has the driver’s safety improved.

Thousands of simulated collision tests and about 100 real crash tests have allowed Volvo Trucks’ engineers to develop a safer truck cab. 
“We’ve utilised new technology, new materials and everything we’ve learned since our most recent new cab. We’ve used all this to build an even safer truck. The result is the world’s safest Volvo,” says Carl Johan Almqvist, Traffic and Product Safety Director at Volvo Trucks.
For instance, high-strength materials such as dual-phase steel have been used in collision-absorbing beams and in the doors. The cab too uses the strongest steel available today for body panelling – ultra-high-strength, thermoset, press-moulded boron steel.
“By using these new grades of steel we can build a stronger cab without increasing its weight. This way, we enhance safety without compromising on payload capacity,” says Robert Ritzén, head of materials in the new cab. 
See the film on www.youtube.com/volvotrucks.

### Customised steel panels

Strength and function are also enhanced with new technology, including laser welding. This method makes it possible to join together two flat panels prior to moulding. 
“As a result, we can customise each panel’s thickness and quality. With this kind of panel, we can optimise the structure and integrate Volvo’s unique safety solutions into the cab,” relates Robert Ritzén.
Several changes in the cab’s structure also boost safety. The cab is now larger since the A-pillars are more upright, creating more room inside the cab for the driver. The door and floor structure has also been altered to provide the best possible protection in a collision. The windscreen is bonded in place. 
“Previously the windscreen served as an emergency exit. Now the roof hatch plays that role,” says  Carl Johan Almqvist.

## The bed: a matter of safety

A safe truck can also be used safely. The new Volvo FH has larger windows and a clearer instrument panel. The field of vision has been increased considerably.  
“What is most important from the viewpoint of traffic safety is that the driver has a good field of vision and can keep his or her eyes on the road. A quick glance at the instrument panel should be enough to give you the information you need,” says Carl Johan Almqvist.
Active systems such as Lane Keeping Support (LKS), Lane Changing Support (LCS), Adaptive Cruise Control and Driver Alert Support (DAS) also contribute to safe driving.
A rested and relaxed driver is also a safer driver. 
“The fact that a comfortable bed benefits traffic safety is probably not the first thought to enter your mind. But a driver who gets a proper night’s sleep and feels rested and alert throughout the working day actually causes fewer accidents,” says Carl Johan Almqvist.

## Safer for car drivers

The Front Under-run Protection System, FUPS, is designed to prevent a passenger car from becoming wedged under the truck in a frontal collision. The protection system in the new Volvo FH represents a major step forward from the safety viewpoint. 
“Volvo fits an energy-absorbing under-run protection system as standard. We have succeeded in improving and reinforcing the system – yet without increasing its weight,” says Carl Johan Almqvist.

## Protection from criminals

The new Volvo FH also spotlights another aspect of safety.
“The truck has several new features that protect the driver against break-ins. Among other things, you can activate the truck’s perimeter lighting using the remote control in the key fob or scare away any thieves hiding nearby by activating the truck’s horn,” says Carl Johan Almqvist.

### What goes into making a safer Volvo FH
Some of the changes that increase safety in the new Volvo FH are: 
• New, stronger materials. For instance ultra-high-strength boron steel
• New technologies such as laser welding 
• New cab structure 
• Improved visibility
• Active safety systems such as Lane Keeping Support, Lane Changing Support, Adaptive Cruise Control and Driver Alert Support (DAS)

September 5, 2012

Link to images:

For further information, please contact:

Lennart Pilskog, Volvo Trucks Global Brand, phone +46 70 3183422

e-mail: lennart.pilskog@volvo.com

Visit http://www.thenewsmarket.com/volvogroup to access broadcast-standard video about the Volvo Group’s various production plants and products. You can download graphic images in the form of MPEG2 files or order them on Beta SP tape. Registration and video are free to the media.

Images are available in the Volvo Trucks image bank http://images.volvotrucks.com

Volvo Trucks provides complete transport solutions for professional and demanding customers, offering a full range of medium to heavy duty trucks. Customer support is secured via a global network of 2,300 dealers and workshops in more than 140 countries. Volvo trucks are assembled in 16 countries across the globe. In 2011 more than 115,000 Volvo trucks were delivered worldwide. Volvo Trucks is part of the Volvo Group, one of the world’s leading manufacturers of trucks, buses and construction equipment, drive systems for marine and industrial applications, aerospace components and services. The Group also provides solutions for financing and service. Volvo´s work is based on the core values quality, safety and environmental care.