Press information

Volvo Trucks introduces Collision Warning with Emergency Brake

Volvo Trucks has developed Collision Warning with Emergency Brake – an advanced emergency braking system equipped with early collision warning to help prevent severe accidents caused by inattention.

Rear-end collisions account for a significant proportion of road accidents. In order to address this problem, Volvo Trucks has developed Collision Warning with Emergency Brake – an advanced emergency braking system which also includes early collision warning. The braking system, which is available on the new Volvo FH Series, has been developed to support the driver so that the majority of these rear-end collisions can be avoided or mitigated.

“We began by asking ‘what really is the problem?’. The answer is inattention. If you watched the traffic ahead of you the whole time, you wouldn’t need systems like these,” says Carl Johan Almqvist, Traffic & Product Safety Director, Volvo Trucks.

The new system combines a radar and a camera that work together to identify and monitor vehicles in front. The system is designed to deal with both stationary and moving vehicles and can prevent a collision with a moving target at relative speeds of up to 70 km/h. When the system detects a vehicle that the truck will hit at its current speed, the warning system activates a constant red light in the windscreen in order to bring the driver’s attention back to the road.

“We don’t want to take over from drivers because we believe they are in the best position to respond, as they might be able to safely drive around the vehicle,” says Almqvist.

However, if the truck fails to detect any reaction from the driver, such as steering or braking, the system upgrades to a flashing red light and a beeping sound. If there is still no reaction, the system applies the brakes gently. When all this fails, the system activates the emergency braking system and does everything possible to bring the truck to a complete stop.

“In the vast majority of cases, the initial warning signals will attract the driver’s attention. And in the rare case that they don’t, the emergency braking system will still help prevent a serious accident,” says Carl Johan Almqvist.

In Europe, emergency braking systems will be a legal requirement in new trucks by November 2015.

Animation of Collision Warning with Emergency break on YouTube

October 5, 2012

For further information, please contact:

Ida Mattsson, Volvo Trucks Global Brand, phone +46 31 323 63 42, e-mail ida.mattsson@volvo.com

Visit http://www.thenewsmarket.com/volvogroup to access broadcast-standard video about the Volvo Group’s various production plants and products. You can download graphic images in the form of MPEG2 files or order them on Beta SP tape. Registration and video are free to the media.

Images are available in the Volvo Trucks image bank http://imagegallery.vtc.volvo.se/.

Volvo Trucks provides complete transport solutions for professional and demanding customers, offering a full range of medium to heavy duty trucks. Customer support is secured via a global network of 2,300 dealers and workshops in more than 140 countries. Volvo trucks are assembled in 16 countries across the globe. In 2011 more than 115,000 Volvo trucks were delivered worldwide. Volvo Trucks is part of the Volvo Group, one of the world’s leading manufacturers of trucks, buses and construction equipment, drive systems for marine and industrial applications, aerospace components and services. The Group also provides solutions for financing and service. Volvo´s work is based on the core values quality, safety and environmental care.