Press information

# The new Volvo FMX:
Groundbreaking innovations for more efficient construction work

## Volvo Trucks reveals the new Volvo FMX at the Bauma exhibition in Munich, Germany. The new construction truck is loaded with innovations that benefit haulers as well as drivers.

“The Volvo FMX gave the construction segment a clear identity and now we are taking a huge step forward in all the most important areas – robustness, handling and design. Everything developed with the driver in focus,” says Claes Nilsson, President of Volvo Trucks.

## The driver in focus

The everyday working conditions of the construction truck driver were in firm focus during the development of the new Volvo FMX. The cab interior has been totally redesigned and a number of innovations make the driver’s job both easier and more efficient.

“Our groundbreaking Volvo Dynamic Steering is a fantastic improvement, especially for a construction driver. It will result in less muscle strain and relive drivers of neck, arm and back aches. Even at low speeds a heavily loaded truck is so easy to manoeuvre that you can steer it with one finger,” says Claes Nilsson.

Among the other new features is a rear air suspension system that provides enhanced comfort and get-you-there ability with excellent ground clearance.

Volvo Trucks is also offering customers a training package specially designed for construction drivers.

## Increased productivity

“Most of the new features are designed to increase the truck’s productivity and durability, something that is very important for customers in this segment. The new air suspension system, for instance, creates excellent drivability and it is tailor made for construction work without any compromises or connection to other segments,” explains Claes Nilsson.

The new Volvo FMX cab is made of high-tensile steel. All components in the front structure have been redesigned – and a large number of them have been moved in order to make the new Volvo FMX more robust in rough construction environments.

## Best construction truck

“With our comprehensive range of specially tailored products and services, the new Volvo FMX is without doubt the best construction truck on the market,” says Claes Nilsson.

Production for European customers will get under way in September 2013. See the film about the new construction truck on http://www.youtube.com/user/VolvoTrucks.

For further information, please contact:

Eva Lindeberger, Volvo Trucks media relations, phone: +46 31 322 8078

e-mail: eva.lindeberger@volvo.com

Visit http://www.thenewsmarket.com/volvogroup to access broadcast-standard video about the Volvo Group’s various production plants and products. You can download graphic images in the form of MPEG2 files or order them on Beta SP tape. Registration and video are free to the media.

Images are available in the Volvo Trucks image bank http://images.volvotrucks.com.

Volvo Trucks provides complete transport solutions for professional and demanding customers, offering a full range of medium to heavy duty trucks. Customer support is secured via a global network of 2,300 dealers and workshops in more than 140 countries. Volvo trucks are assembled in 16 countries across the globe. In 2012 more than 105,000 Volvo trucks were delivered worldwide. Volvo Trucks is part of the Volvo Group, one of the world’s leading manufacturers of trucks, buses and construction equipment, and drive systems for marine and industrial applications. The Group also provides solutions for financing and service. Volvo´s work is based on the core values quality, safety and environmental care.