4.  KIA CEE’D HYBRID

Prototype fleet of Kia cee’d Hybrids to begin testing

In parallel with its on-going domestic Korean and USA-based FCEV vehicle testing programmes, Kia Motors is producing a fleet of prototype Kia cee’d Hybrid cars especially for testing and evaluation in Europe and North America.

First shown at the Paris Show last year, the Kia cee’d Hybrid has been created by Kia R&D to take part in ‘real-world’ test activities.  Like the Soul Hybrid (also shown at Paris), the cee’d uses an upgraded powertrain developed from the earlier Rio Hybrid.  The cee’d Hybrid now features Kia’s Gamma 1.6-litre gasoline engine, mated to a 15kW (20 ps), 105 Nm AC synchronised electric motor, Kia’s own CVT (continuously variable transmission) and Kia’s new ISG (Idle Stop & Go) system.

The high-torque electric motor generates its maximum torque (105 Nm) from just 1500 rpm and the Li-Poly 180 volt, 5.3 Ah power pack is located at the side of the trunk.  The computer-controlled ISG system also allows fuel-saving stop/start motoring.

Kia calculates that the cee’d Hybrid accelerates from 0-to-100 kph in 11.8 seconds and can reach a top speed of 185 kph.  The prototype achieves fuel consumption of 4.81 litres per 100 km and a CO2 figure of 109 g/km.  Compared to the standard 1.6-litre gasoline cee’d, CO2 emissions are reduced by 25.0%.

Ends