CERATO 5-DOOR TECHNICAL SPECIFICATIONS [ General Markets* ]

2011 Kia Cerato 5-door Hatchback

Body & Chassis

Five-door, five-seater hatchback with all-steel unitary construction bodyshell.  Choice of two transversely-mounted gasoline engines driving the front wheels via a six-speed manual or six-speed automatic transmission.

Gasoline Engines

2.0-litre / 156 ps

Name  			Theta II (4-in-line)

Type			DOHC, four-cylinder, with CVVT

Capacity 		2.0-litres, 1998 cc

Max power 		156 ps (114.7 kW) @ 6200 rpm

Max torque 		194.2 Nm (19.8 kg.m) @ 4300 rpm

1.6-litre / 124 ps

Name 			Gamma (4-in-line)

Type 			DOHC, four-cylinder, with CVVT

Capacity 		1.6-litres, 1591 cc

Max power 		124 ps (91.2 kW) @ 6300 rpm

Max torque 		156.5 Nm (15.9 kg.m) @ 4200 rpm

Transmissions

2.0 MT	 	2.0 AT		1.6 MT		1.6 AT

Type	 		6-sp		6-sp 		6-sp		6-sp

Suspension & Damping

Front 	Fully independent by MacPherson struts, with coil springs and gas-filled shock absorbers. Anti-roll stabiliser bar.

Rear 	Coupled torsion beam rear axle, with coil springs and gas-filled shock absorbers.

Steering

Standard

Type 			Hydraulic power-assisted rack and pinion

Gearing 		2.89 turns lock-to-lock / 2.77 (with 17-inch wheels)

Turning circle 		10.32 metres / 10.78 metres (with 17-inch wheels)

Optional

Type 			Electric (motor driven) power-assisted rack and pinion

Gearing 		2.80 turns lock-to-lock / 2.68 (with 17-inch wheels)

Turning circle 		10.32 metres / 10.78 metres (with 17-inch wheels)

Brakes

Front 	 		280 x 26 mm ventilated discs

Rear 			203 x 8 mm drum (standard)

262 x 10 mm solid discs (optional, standard on SX)

ABS 	4-Channel anti-lock system with EBD (optional, standard on SX)

Wheels & Tyres

Standard  		Steel 15 in x 5.5J 	195/65 R15 tyres

Options 		Alloy 15 in x 5.5J 	195/65 R15 tyres

Alloy 16 in x 6.0J 	205/55 R16 tyres

Alloy 17 in x 7.0J	215/45 R17 tyres

DIMENSIONS (mm)

Exterior

Overall length 		4340 		Overall width 		1775  (excl. door mirrors)

Overall height 		1460  		Wheelbase 		2650

Front overhang	  895 		Rear overhang 	  795

Front track 		1557 		Rear track 		1564

Interior			Front 		Rear

Headroom 		1015		  975

Legroom 		1100 		  890

Shoulder room 	1415 		1390

Hip room 		1345 		1355

Capacities

2.0 MT		2.0 AT		1.6 MT 	1.6 AT

Fuel tank (litres)	52.0		52.0		52.0		52.0

Luggage (SAE) 	415 litres  (all seats upright)

Weights (kg)

Curb weight (min.)	1302 		1328 		1253 		1287

Gross weight 		1760		1780 		1700 		1740

Performance

Top speed / kph 	190 		190		190		190

0-to-100 kph / sec 	  9.1		  9.8		10.3		11.5

Fuel Economy (litres/100 km)**

Overall			  7.4 		  7.5		  6.4		  6.8

CO2 g/km		177 		179		152		164

* Kia Motors marketing classifies the following countries & regions as ‘General Markets’ – Central & South America, the Caribbean, Asia (excluding China), Pacific (including Australia), the Middle East and Africa.

** Manufacturer’s estimated figures based on 15-inch tire equipped vehicles