GENEVA MOTOR SHOW 2011

Kia Optima Hybrid

Optima Hybrid drives Kia forward into ‘EcoDynamics’ era

- Optima Hybrid pioneers new technologies for future models

- Ingenious, simple and cost-effective ‘parallel hybrid’ system

- 0-to-100 kph in 9.2 sec, plus a 40.7% fuel consumption improvement

Following its world premiere at the Los Angeles Auto Show in the USA just a few weeks ago, Kia is exhibiting its all-new Optima Hybrid sedan in front of a European audience for the first time at the Geneva Motor Show, raising Kia’s environmental credentials to a new level.

Taking Kia forward into its ‘EcoDynamics’ era, the new Optima Hybrid is another major step towards the company’s goal of manufacturing and marketing environmentally-friendly personal transport for future generations.

Although it has been created primarily with the US market in mind, the Optima Hybrid pioneers new technologies which are destined to appear in other Kia production models around the world as the decade unfolds.

Scheduled to begin mass production in the first half of 2011, the Optima Hybrid employs a truly innovative Kia-developed hybrid powertrain that delivers a unique blend of performance – acceleration to 62 mph (100 kph) in 9.2 seconds and a top speed of 121 mph (195 kph) – plus class-leading fuel economy, achieving a 40.7% fuel consumption improvement compared with a regular U.S. version Optima.

The Kia Optima Hybrid is equipped with an ingenious, simple and cost-effective ‘parallel hybrid system’.  The 2.4-liter gasoline engine is paired with a small electric motor and drives the front wheels via a six-speed automatic transmission – without the traditional torque converter.

A special clutch is fitted between the Optima Hybrid’s gasoline engine and the electric motor, enabling the gasoline engine to be de-coupled from the powertrain so the sleek sedan can be operated in zero-emissions, full-electric drive mode from standstill up to 62 mph.  Furthermore, the system’s configuration does not require a high-capacity electric motor and generator, saving both weight and cost.

Seamless driving for everyday motoring

When setting off, the Optima Hybrid operates in Electric Mode.  As vehicle speed increases, the Hybrid Starter motor/Generator (HSG) starts the gasoline engine and the clutch is closed, allowing the engine to take over the task of powering the car.  The electric motor switches into hybrid operation and serves as either a secondary engine (during full acceleration and hill-climbing) or a generator (during cruising and deceleration) to recharge the battery pack as necessary.  Whenever the car comes to a stop for more than a few seconds, the gasoline engine automatically shuts off to conserve fuel and minimise emissions.

When braking, the electric motor converts kinetic energy into electricity for storage in the battery pack.  The 8.5 kW HSG also functions as a generator to re-charge the battery pack if the state of charge is low when the car is stationary.  Throughout the entire driving experience, in everyday motoring, under all conditions, the hybrid operation is automatic and seamless.

A responsive and rewarding drive is guaranteed by the Optima Hybrid’s 30kW Interior Permanent Magnet (IPM) synchronous electric motor, which produces 40.7 ps and 205 Nm of torque from 0-to-1,400 rpm in electric mode, and the combined (electric motor plus gasoline engine) hybrid powertrain output of 209 ps and 265 Nm of torque.

State-of-the-art batteries & optimised engine

Kia’s Optima Hybrid employs a lithium polymer battery array developed in partnership with LG Chem.  Lithium polymer is ideal for automotive applications and these new batteries provide an optimum balance between power delivery, energy density and thermal stability.  Reliability is so good that the Optima’s battery pack will not need replacing during the vehicle’s lifespan – at least 10 years and 150,000 miles.

Taking advantage of the additional, instant and continuously available torque from the electric motor, Kia has modified its popular four cylinder 2.4-litre Theta II engine to maximise its efficiency and achieve a 10% fuel saving over a regular Theta engine.

For the Optima Hybrid, Kia has modified the six-speed automatic transmission found on the conventional Optima for hybrid application.  The traditional torque converter is replaced with the electric motor and a high-efficiency oil pump.  This allows EV mode operation, maximizes regeneration of kinetic energy during braking and also provides a more responsive drive than competitors’ CVT systems.

A product of Kia’s Eco-Technology Research Institute near Seoul, together with the Namyang Research and Development facility and a unique collaboration between numerous Kia facilities around the world, the ‘full parallel hybrid system’ created for the Optima Hybrid will be further developed for use in forthcoming Kia models during the next decade.

-Ends-

TECHNICAL SPECIFICATIONS

Kia Optima Hybrid

Body & Chassis

Four-door, five-seater mid-sized sedan, with all-steel unitary construction bodyshell.  Powered by parallel hybrid powertrain system consisting of transversely-mounted gasoline engine mated to electric motor driving the front wheels (2WD) via a six-speed automatic transmission.

Engine

2.4-litre CVVT / 209 ps Gasoline

Name 			‘Theta II’

Type 			In-line four cylinder, with 30 kW parallel electric motor

Capacity 		2.4-litres, 2,359 cc

Max power 		209 ps (153.7 kW) @ 6000 rpm

Max torque 		265 Nm (27.03 kgm) @ 4250 rpm

Bore x Stroke 		88 x 97 mm

Compression ratio	13.0:1

Fuel system 		MPI (multi-point injection)

Construction 		Aluminium cylinder block and head

Emissions class 	N/a

Electric motor

30 kW electric motor powered by long-life 270 V lithium polymer battery pack

Transmissions

Type			Six-speed automatic

Gear Ratios (Automatic)

1st			4.212

2nd			2.637

3rd			1.800

4th			1.386

5th			1.000

6th			0.772

Reverse 		3.385

Final Drive 		3.320

Performance and economy

0-100kph (62 mph)	9.2 seconds

Top speed		195 kph (121 mph)

City			35 mpg *

Highway		40 mpg *

Combined		37 mpg *

*Consumption figures are based on US EPA official cycle (US gallons)

Suspension & Damping

Front 	Fully independent by subframe-mounted MacPherson Struts, with coil springs and twin-tube gas-filled shock absorbers.

24 mm diameter anti-roll stabiliser bar.

Rear 	Fully independent by subframe-mounted multi-links, coil springs and twin-tube gas-filled shock absorbers.  Standard ASD shock absorbers.

15 mm diameter anti-roll stabiliser bar.

Steering

Type 			MDPS Electric power-assisted rack and pinion

Gearing 		2.94 turns lock-to-lock

Turning circle 		10.45 metres (minimum)

Brakes

Power 			Single 10.5-inch booster (LHD)

Front 	  		300 x 28 mm ventilated discs 	(16-inch/17-inch wheels)

320 x 28 mm ventilated discs 	(18-inch wheels)

Rear			284 x 10 mm solid discs

Parking brake 		Foot operated pedal

EPB, electronic parking brake  (optional)

ABS 			4-channel anti-lock system with EBD

BAS			Boosts braking power during emergency stops

Wheels & Tyres

Alloy 16 in x 6.5J	205/65 R16 tyres

Alloy 17 in x 6.5J 	215/55 R17 tyres

Spare (standard) 	Tyre mobility kit

Spare (optional)	Full-size alloy wheel and tyre

DIMENSIONS

Exterior (mm)

Overall length		4845 		Overall width* 		1830

Overall height		1450 		Wheelbase 		2795

Front track		1601**  	Rear track 		1601**

Front overhang	965 		Rear overhang 	1085

Ground clearance 	135

*excluding door mirrors

**from 1595-to-1601 mm, depending on wheel/tyre combination

Interior (mm)		Front 		Rear

Headroom 	 	1015 		 955

Legroom 	 	1155 		 880

Shoulder room  	1455 		1415

Hip room 	 	1388 		1384

Capacities

Fuel tank 		65 litres

Luggage (VDA) 	280 litres

MARCH 2011