ALL-NEW

KIA CARENS

Press Information

General Markets

January 2013

ALL NEW KIA CARENS

GENERAL MARKETS

Contents

1	Introduction

All-new Carens delivers stylish, spacious practicality

2	Styling & Design

Sleek aerodynamics and a dramatic cab-forward design

3	Comfort & Convenience

Generous standard equipment with an extensive options list

4	Practicality

Up to seven seats with great people/cargo versatility

5	Engines

Gasoline and diesel power from 134 to 152 ps

6	Transmissions

Six-speed transmissions for every new Carens

7	Running Gear

Engineered for agility, stabilty, comfort and refinement

8	Safety

A stronger structure and enhanced safety standards

9	Equipment

Comprehensive equipment details, model by model

10	Technical Specifications

Full technical details of model line-up

1.  INTRODUCTION

All-new Carens delivers stylish, spacious practicality

The all-new Kia Carens is a compact MPV designed and engineered from a clean sheet to meet the needs of modern families.  With sleek aerodynamics and a cab-forward design it blends contemporary and distinctive exterior styling with a fresh and trendy interior.

Offering customers in General Markets a choice of three powertrains, up to seven seats and a broad range of convenience and safety features, the new third-generation Carens is set to attract even more customers to the Kia brand.

“The all-new Carens takes Kia back into one of the most important and competitive sectors of the global market with a strong contender for class-honours.  Very stylish and sporty looking, new Carens has a spacious and versatile interior with five or seven seats, a large cargo bay and storage compartments throughout the cabin,” comments Thomas Oh, Kia’s Executive Vice President & COO of the International Business Division.

“This model will have great appeal to families with an active lifestyle who don‘t want to compromise between style and practicality.  It is destined to attract many new customers to our showrooms and introduce them to the benefits of Kia ownership,” adds Mr Oh.

Measuring 4.5-meters long, the new Kia Carens is a more compact, but also more spacious vehicle than the previous generation model.  Cabin space is generous thanks to the new model’s increased wheelbase (up by 50 mm, to 2750 mm), skilful packaging and cab-forward design which places the base of the A-pillar above the front-wheel center line.  Overall, new Carens is 20 mm shorter, 15 mm narrower and 40 mm lower.  Its overall height (1,610 mm) is the same as the Kia Soul and is one of the lowest in class – giving the model an especially sporty appearance.  The contemporary styling of new Carens is also highlighted by its standard LED positioning lights.

Despite the economic situation in some countries, Kia anticipates that global demand for C-segment MPV models will continue to rise over the next three years.  Compact MPV sales totalled 1.9 million (all brands) around the world in 2012, and Kia predicts that this segment will grow to 2.27 million in 2014 (up 19.6%) and go on to pass the 2.5 million mark in 2015.

Sales of the second-generation Kia Carens between 2006 and 2012 reached 420,000 units.  When new Carens is on sale in all markets (2014) Kia is planning to manufacture 105,000 units annually – exclusively supplied from its Gwang-ju plant in Korea.

*General Market

General Market countries include the regions of Central and South America, the Caribbean, Asia (excluding China and Korea), the Pacific, Middle East and Africa

2.  STYLING & DESIGN

Sleek aerodynamics and a dramatic cab-forward design

The all-new Kia Carens is a completely fresh model from the ground up, and its sleek and sculpted design marks a dramatic shift away from the look of its predecessor.  It builds on the functionality and versatility of the original Carens, with a spacious five or seven seater layout, a generously proportioned luggage bay and numerous stowage spaces, and wraps this family-friendly adaptability in more purposeful sheet metal.

“I wanted to give the new Carens a sleeker look and feel, to create a design that envelops its functionality and versatility in something altogether more athletic and dynamic,” says Peter Schreyer, President and Chief Design Officer, Kia Motors.

“This new-found visual dynamism is important – this car needs to look appealing and attractive – but during its design and development stages, we never lost sight of the fact that packaging flexibility and adaptability are the reasons why people buy this type of vehicle,” comments Schreyer.

Both Schreyer and Gregory Guillaume, Kia’s Chief Designer Europe, are candid when discussing the design of the new Carens.  “A vehicle like the Carens is probably one of the hardest of all to get right, in terms of styling, because we are very tightly constrained by the car’s functionality.  That packaging versatility cannot in any way be compromised by the design of the car, because to do so would eradicate the car’s raison d'être,” comments Guillaume.

Schreyer and Guillaume’s team created subtle styling cues to enhance the new Carens’ elegant and balanced proportions and deliver an air of sophistication and refinement.  As an example, Schreyer singles out the understated chrome beltline strip that runs from the base of the windscreen, along the lower level of windows and curls up to meet the C-pillar.  “This element not only adds a premium feel to the clean-cut exterior, but also creates a visual link with the new Sportage, which features the same design motif,” he explains.

One of Schreyer’s design goals was improved visibility – a key element for safe driving, particularly in congested urban areas.  “The base of the new Carens’ windscreen is very low and this works with the front quarter windows and the low and wide sweeping dashboard design to deliver excellent visibility,” adds Schreyer.  The available panoramic glass roof that floods the cabin with light further enhances the interior’s sense of spaciousness.

Similarly, the Carens design team worked hard on ensuring the front and rear overhangs (940 and 835 mm respectively) were kept as short as possible to boost manoeuvrability when parking and negotiating city traffic.

Neat styling touches abound – the integrated roof rails, the sleek rear spoiler, the 60/40 split second-row seats that feature fore and aft adjustment, and Kia’s tactile new steering wheel.

“With its perfect balance of proportion, style and functionality, the distinctive new Carens marks yet another successful and stylish step for Kia’s global design team,” says Schreyer proudly.  “There’s a design honesty here – the Carens is neither over-dressed nor does it feature contrived design elements.  It’s a car cleanly and elegantly defined by its functionality.”

New Carens’ external size and proportions, together with careful attention to surface detailing and airflow-smoothing panels beneath the car, have cut the Kia MPV’s aerodynamic drag to Cd 0.30 (down from 0.32 for the previous model).

Depending on individual market preferences, the new Kia Carens will be available in a choice of up to eight exterior colours – Clear White (solid), Bright Silver (metallic), Titanium Silver (pearl metallic) and Cherry Black (pearl), plus four new colours: Newport Blue (pearl), Camden Beige (pearl metallic), Galaxy Brown (pearl metallic) and, later in the year, Inferno Red (metallic).

3.  COMFORT & CONVENIENCE

Generous standard equipment with an extensive options list

The all-new Carens is a truly innovative compact MPV which introduces a wealth of up-to-date, new comfort and technical features to advance every aspect of every journey for all occupants.

While the new Carens is a family-focused vehicle, driver comfort in every model is assured thanks to the tilt-and-telescopic adjustable steering wheel, height adjustable driver’s seat and the adoption of an organ-type accelerator pedal pivoting on the floor and moving in a way that matches the natural motion of the human foot.

In most countries, new Carens will be available as an LX or as a higher-specification EX model – with five or seven seats – and a wide range of factory-fitted options.

The Carens LX model is generously equipped as standard with LED front positioning lights, manual air-conditioning, rear (2nd row) heating and cooling air vents, electric windows (front and rear), a total of six audio speakers and an anti-theft alarm.

Customers choosing the Carens EX gain 16-inch alloy wheels, privacy glass, front fog lamps, special ‘clean tex’ (easy-clean) seat upholstery, fold-up front seatback tables and a forward folding front passenger seat – to accommodate long items of luggage.

Depending on model (see Section 9), exterior options will include 17- and 18-inch alloy wheels, HID Xenon headlamps, LED front and rear lights, a chrome beltline molding, a three-part tilt-and-slide panoramic glass sunroof and puddle lights, plus front and rear parking sensors.

From a long list of interior options, customers can specify a heated steering wheel (not available in Middle East region), heated front and second row seats (2nd row seat warmer not available in Middle East region), ventilated front seats, automatic climate control air-conditioning, cruise control, 10-way powered driver’s seat with an extendable cushion (to optimize thigh support), a 4.3-inch TFT LCD touch-screen audio system, a Supervision instrument cluster with a 4.2-inch TFT LCD screen and high-definition graphics, manual integrated side window blinds and a special wide-angle ‘conversation mirror’ in the overhead console (which allows parents to safely monitor their children) and a black (rather than beige) cabin headlining.

Customers will be offered a choice of Black (one-tone) or Black & Beige (two tone) interior colour schemes for the seats and cabin trim, in regular cloth, woven cloth or leather – depending on model.  Buyers of the EX will also be able to order new ‘hydro-graphic technical pattern’ trim accents for the steering wheel, dashboard, center console sides and upper door trims.

4.  PRACTICALITY

Up to seven seats with great people/cargo versatility

For the all-new Carens, the longer (2,750 mm) wheelbase and the latest packaging technologies have resulted in a spacious cabin with generous room for up to seven occupants and a larger cargo bay.

To deliver the maximum carrying versatility expected by MPV customers, the front passenger seat backrest can be folded forwards, the second row features sliding/folding seats with a 60/40 split and the third row seats (in seven-seater models) split 50/50 and fold flat into the trunk floor when not required.  In the seven-seater Carens, the second row seats can slide forwards by 240 mm to give easy access to the third row seats.

Trunk space is increased by 16.8% (compared to the previous model), thanks to the compact design of the CTBA rear suspension which replaces the previous model’s multi-link system.  The intrusion of the rear wheel arches is greatly reduced, so that the width of the trunk floor is increased by 67 mm to 1,080 mm.  The cargo bay is also 24 mm longer (999 mm) and 48 mm taller (499 mm up to the window) than before.  To ease the task of loading cargo, the top of the rear bumper has been lowered by 15 mm.

With seven seats occupied, minimum cargo capacity is 103 liters.  With the front and second row seats in use, capacity is increased to 492 liters (seven-seater) and to 536 liters in the five-seater model which has a lower trunk floor.  Up to 1,667 liters of cargo can be carried when only the front seats are occupied.  By folding the front passenger seat backrest down, objects up to 2,150 mm long can be accommodated.

To meet the additional cargo hauling demands of vacations or moving house, new Carens can carry up to 100 kg on its roof, and has a towing capability between 730 and 1,500 kg – depending on model and trailer type.

Numerous storage spaces within cabin

To ensure that new Carens delivers the maximum versatility demanded by modern active family lifestyles, a total of 13 storage spaces are provided within the cabin.

At the front, glove box capacity is increased 23% (to 8 liters), center console capacity is up 84% (to 4.8 liters), and the small console tray (ahead of the gear selector) holds 1.3 liters.  Two large cupholders are fitted front and rear.

In the back, two new underfloor storage trays (in the second row foot wells) each have a 6.8-liter capacity.  New storage pockets in each door can hold 1.0-liter (front) and 0.6-liter (rear) bottles.

5.  ENGINES

Gasoline and diesel power from 134-to-152 ps

In most General Market countries, all-new Carens customers will have a choice of three four-cylinder engines.  Two gasoline engines and one diesel power unit offer a broad power spread, ranging from 134 ps to 152 ps, together with competitive fuel economy and CO2 emissions from as low as 144 g/km for the manual diesel model.

Both gasoline engines – Kia’s 2.0-liter Nu engine and the popular 1.6-liter Gamma engine – are lightweight units which feature cast aluminum cylinder blocks and aluminum cylinder heads.  Both are equipped with an offset crankshaft (to reduce friction), a low-noise timing chain, mechanical lash adjustment, variable intake valve timing (and exhaust valve timing on the Gamma), and a plastic variable intake manifold (on the Nu engine).

The 2.0-liter Nu unit delivers a maximum of 152 ps at 6500 rpm and 19.8kg·m of torque at 4800 rpm.  It features DOHC, 16 valves and MPI (multi-point fuel injection).

Fitting the 1.6-liter Gamma engine with ‘GDI’ (gasoline direct injection) boosts its power and torque outputs without increasing fuel consumption.  For new Carens, the engine is tuned to generate a maximum of 134 ps and 16.6 kg·m.

The fastest accelerating new Carens is the 2.0-liter gasoline model which reaches 100 kph in 9.9 seconds (manual), while the 1.6-liter takes 11.3 seconds.  Top speeds range from 178 to 200 kph across the line-up.

Modifications to both these gasoline engines have resulted in lower CO2 emissions – down to as little as 177 g/km for the 2-liter, a significant improvement over its predecessor.

The U2 1.7-liter diesel engine is already popular in a variety of Kia vehicles around the world and in new Carens it will be available in its ‘high power’ form.  This unit produces maximum power of 136 ps and 33.7 kg·m of torque from just 1750-2500 rpm with the manual transmission, or 32.6 kg·m with the automatic transmission.  With diesel power, the Carens reaches 100 kph in 10.4 seconds (manual) and 12.0 seconds (automatic).

6.  TRANSMISSIONS

Six-speed transmissions for every new Carens

Matching customers’ rising expectations, every all-new Carens will be fitted with a six-speed transmission and every model will offer drivers a choice of manual or multi-mode automatic gearboxes.

Engineered to optimise the balance between performance and economy, the new transmissions feature lower first and second gear ratios (to boost acceleration from standstill), and high top (sixth) gear ratios allowing lower engine revs during high-speed cruising – reducing cabin noise and enhancing refinement, while also lowering both fuel consumption and CO2 emissions.

First-gear ratios are as low as 3.769:1 (manual) and 4.400:1 (automatic), while top gear ratios are as high as 0.729:1 (manual) and 0.772:1 (automatic).

For fitment in new Carens the completely new six-speed manual gearbox features smoother shifting, enhanced efficiency (reducing fuel consumption), and greater durability.  Improvements include triple-cone synchronizers, quieter running optimized gear teeth, shorter shift strokes between ratios, a new reverse gear selection ‘button’, hydraulic clutch control and low viscosity oil – ensuring that the transmission does not require any servicing for the life of the vehicle.

Both the gasoline and diesel engines will be offered with an optional six-speed automatic transmission engineered and manufactured in-house by Kia.  Replacing the previous model’s four-speed unit, the new automatic delivers faster acceleration from low speeds and greater refinement at high speeds.

This transmission features two operating modes – ’Fully Automatic’ or ‘Sport’.  For city driving, fully automatic mode is ideal.  The selector gate is a straight P-R-N-D arrangement, with Sport mode engaged by moving the lever towards the driver when in D.  Sport mode allows for clutch-less sequential manual gear changes for greater driver involvement – either by pushing the selector lever (forwards for up, back for down), or by using the optional paddle-shifts on the steering wheel. In addition, paddle shifters are available on the 2.0 gasoline and 1.7 diesel with automatic transmission.

Thanks to the new Carens’ 58-liter fuel tank, owners should enjoy a typical range of 650 km between fill-ups.

7.  RUNNING GEAR

Engineered for agility, stability, comfort and refinement

The suspension and running gear of the all-new Carens have been comprehensively re-engineered and developed to deliver responsive handling, excellent straight-line stability, and exceptional ride quality and refinement on a wide variety of surfaces.

New Carens is equipped with MacPherson strut front suspension mounted on an all-new sub-frame to isolate the cabin from road shocks.   A decreased tie road linkage angle from 10.9 to 8.0 degrees and increased king-pin offset from -8.45 to -14.67 mm enhance straight driving stability and improve vehicle self-centering.

At the rear, the new CTBA (coupled torsion beam axle) – which replaces the previous multi-link system – features a vertically mounted shock absorber with a new impact-absorbing top mounting.  The system is engineered with a strong connection between the trailing-arms and the stub-axles, and designed to reduce under-steer and bump-steer, while delivering a comfortably compliant ride.

The MDPS electric power-assisted rack-and-pinion steering features a combined torque/angle sensor to protect against side wind gusts.  The steering’s gearing is unusually ‘quick’ for this type of vehicle with just 2.7 turns lock-to-lock to deliver responsive handling.

Kia’s new Flex Steer system is fitted as standard.  This offers three different steering weights to match customer preference with Normal, Sport and Comfort modes – while leaving the gearing unchanged.

For General Markets, new Carens will feature an all-disc braking system – with 300 mm ventilated front, and 284 mm solid rear discs – as standard on all models.  The performance of the braking system can be supported by ABS anti-lock, electronic brake force distribution and BAS emergency ‘brake assist’ systems.  Kia’s tests have demonstrated that braking from 100 kph takes 40.8 metres.

The standard wheel and tire package for new Carens is a 16-inch steel wheel with 205/55 R16 low rolling resistance tires, or similar size alloy wheels – depending on model.  To suit customer preference, new wider 17-inch silver five double-spoke alloys and 18-inch black/machine polished alloy wheels with lower-profile (225/45 R17 and 225/45 R18) tires will be available as options.

8.  SAFETY

A stronger structure and enhanced safety systems

Kia has a strong record for producing vehicles that offer customers high levels of active and passive safety technology.  The all-new bodyshell created for the latest Carens incorporates Kia’s latest CAD techniques and structural lessons learned from recent Kia models, especially the new-generation Cerato and Forte models.

Manufactured with a high percentage 35.9% of high-strength steel, the new bodyshell is expected to achieve a 5-Star rating in Euro NCAP crash safety tests and a top score in other official national safety tests.

Computer-aided design was employed to devise a three-way path to disperse frontal impact forces.  The longitudinal engine bay chassis members are formed from 120 kg class high-strength steel and constructed using large diameter welds.  The bodyshell’s side sills are also built from 120 kg steel.  A major change in the construction method for new Carens is the introduction of structural adhesives, with more than 40 meters of adhesive applied.

The new Carens’ bodyshell also benefits from additional cross members linking the front suspension towers, and forming ring-shaped structures at the base of the B-pillars, the C-pillars and around the tailgate opening.

Hot stamping is used to manufacture the B-pillars in 150 kg class steel.  This production method heats steel to 900º C, then rapidly cools the steel, while simultaneously pressing it into immensely strong components with greatly enhanced crashworthiness – without adding weight.

Torsional rigidity of the new bodyshell is increased by 64% (over the previous model), bringing the added benefits of improving refinement and creating a stronger foundation for the suspension and steering – in turn enhancing ride comfort and steering precision.

New ‘crash boxes’ are fitted to the longitudinal engine bay side members, reducing low-speed impact damage, and the rear chassis side members are strengthened – minimizing distortion and reducing repair costs.  An additional benefit of the CTBA rear suspension layout is that its robust structure provides the under-seat fuel tank with added protection during a rear impact.

Advanced technology to match customers’ preferences

Available active safety equipment includes: an all-disc braking system with ABS anti-lock, BAS brake force assist system, ESC electronic stability control, HAC hill-start assist control and a VSM vehicle stability management system.

Standard passive safety kit for new Carens includes a driver’s airbag, three-point seatbelts for all but the center 2nd row seat and height-adjustable head restraints for all occupants.  Options include side and curtain airbags and speed-sensing automatic door locks.

Front and rear parking sensors are available.  Safety during parking manoeuvres can be enhanced even further by using the optional rear-view safety camera, while visibility during night-time driving can be enhanced by specifying HID Xenon headlamps.

To maximize visibility at all times, new Carens is fitted with an ‘opposing-type’ windscreen wiper system, with the left and right blades synchronized to rise in opposite directions, each sweeping to the A-pillar and cleaning an area which is 10% larger than with conventional systems.

Ends

Editors’ Notes

All-new Kia Carens range

Some markets may select particular powertrains and levels of equipment to suit the preferences of their local consumers.  Please check the final technical specification and model equipment details with your national Kia PR representative.

9.  STANDARD & OPTIONAL EQUIPMENT / GENERAL MARKETS

Standard Equipment

Kia Carens LX

Exterior

- 16-inch steel wheels with 205/55 R16 tires

- Black and chrome radiator grille

- Body-color bumpers (4.0 kph / 2.5 mph, impact resistant)

- Body-color door handles

- Black door mirror mountings

- Black beltline molding

- Body-color tailgate garnish

- Body-color rear spoiler

- Projection-style headlights

- LED front positioning lamps

- Manual-adjustable headlamp levelling

- Tinted glass

- Heated rear window

- Rear window washer & wiper system

- Roof-mounted micro radio antenna

- LED high-mounted stop light

Comfort & Convenience

- MDPS electric power steering with three-mode FlexSteer

- ‘Escort’ light function

- Manual air-conditioning

- Heating and ventilation system with 4-speed fan

- Rear heating and ventilation ducts (2nd row seats)

- Tilt-and-telescopic adjustable steering wheel

- Electric adjustable door mirrors

- Tachometer (rev counter)

- Exterior temperature display

- Trip computer and odometer

- Remote central locking

- Remote fuel-filler flap release

- Remote trunk lid release

- Cabin courtesy room lamp delay

- Luggage Lamp

- Luggage net hook

- Four 12 V power outlets: Front console (2), rear vent (1), luggage room side (1)

- Active ECO fuel-saving program (automatic transmission models)

Interior

- 3-spoke soft polyurethane steering wheel

- Black or Beige Knit cloth-covered seat upholstery

- Chrome door handles

- Height-adjustable driver’s seat

- Front seatback storage pockets

- Front and rear door map pocket & bottle holder

- Electric front and rear windows (auto-down, driver’s only)

- Dual front sunvisors with covered vanity mirrors

- Glove box with illumination

- Center console storage with armrest

- Two front cup-holders

- Folding 2nd row centre armrest with two cup holders

- Overhead sunglass storage

- Overhead map-reading lamp

- Digital clock

- 60/40 split 2nd row seats

- 3:3:3 individual 2nd row seats (Australia only)

- 50/50 split 3rd row seats  (7-seater only)

- 2nd row under-floor storage areas

- Four door-mounted audio speakers

- Two front tweeter speakers

Safety & Security

- De-powered Driver’s front airbags

- 3-point seatbelts for front and outside 2nd row and 3rd row seats

- 2-point seatbelt for center 2nd row seat

- Height-adjustable head restraints for all seats

- Child-safety rear door locks

- Audible seatbelt reminder (Australia only)

- Burglar alarm

Kia Carens EX

Additional factory-fitted standard equipment over LX model

- 16-inch alloy wheels with 205/55 R16 tires

- Body-color outside rear-view mirror

- Roof rack

- Privacy glass (rear doors / tailgate / rear quarter glass)

- Front fog lamps

- Woven & Clean Tex cloth-covered seat upholstery

- Leather wrapped steering wheel and gear lever shroud

- Electric adjustable, heated, folding outside rear-view mirror

- Fold-up front seatback tables

- Forward folding front passenger seatback

- Low washer fluid warning

Optional Equipment

Different markets may select some of the ‘factory-fitted options’ for fitment as standard equipment on the all-new Kia Carens models for their region.

Please check with your local Kia PR representative for the definitive equipment specifications in your country.

Kia Carens  (all models)

Exterior

- 17-inch alloy wheels with 225/45 R17 tires

- Panoramic glass powered tilt’n’slide sunroof

Comfort & Convenience

- Rain-sensing windshield wipers

- Auto light control

- Air-conditioned glove box

- Cruise control with speed limiter

Interior

- Three-stage heated front seats

- Heated 2nd row seats

- Instrument and center console lighting rheostat

- Radio / CD player with MP3 compatibility

- AUX, USB connectivity

- Audio remote controls on steering wheel

- Bluetooth® handsfree without voice recognition

Safety & Security

- Front passenger, front side and curtain airbags

- Rear-view safety camera

- Speed-sensing automatic door locking

- Anti-theft engine immobilizer

- Rear parking sensors

- ESC (Electronic Stability Control)

- BAS (Brake force Assist System)

- HAC (Hill-start Assist Control)

- VSM (Vehicle Stability Management system)

Kia Carens  (LX only)

Exterior

- 16-inch alloy wheels with 205/55 R16 tires

- Body-color outside rear-view mirror

- Roof rack

- Front fog lamps

- Electric adjustable & heated outside rear-view mirror

Interior

- Leather wrapped steering wheel and gear shift knob

- Low washer fluid warning

Kia Carens  (EX only)

Exterior

- 18-inch alloy wheels with 225/45 R18 tires

- Black glossy and chrome front radiator grille

- Chrome belt line molding

- Chrome tailgate garnish

- Chrome door handles

- Side-repeater lights in outside rear-view mirrors

- HID Xenon headlamps

- LED daytime running lights

- LED rear combination lights

Comfort & Convenience

- Rear side window sunblinds

- 10-way powered driver’s seat with cushion extension

- Powered adjustable lumbar support (driver’s seat)

- Smart entry with engine start/stop button

- Puddle lights

- Automatic dual-zone air-conditioning

- Automatic windshield de-fogging system

- Steering-wheel mounted Paddle Shift (automatic models)

Interior

- Black cabin headliner

- Ventilated front seats with seat warmer

- SuperVision instrument cluster

- Conversation/child monitoring cabin mirror

- Leather seat upholstery

- Front foot  lamps

Safety & Security

- Front parking sensors (with Rear Parking Assist System)

- Electronic parking brake

10.  TECHNICAL SPECIFICATIONS / GENERAL MARKETS

All-new Kia Carens

Body and chassis

Five-door, five- or seven-seater MPV, with all-steel unitary construction bodyshell.  Choice of transversely mounted diesel and gasoline engines driving the front wheels via a six-speed manual or automatic transmission (depending on model and market).

Engines  (availability may vary by individual markets)

Gasoline

2.0-litre 152 ps

Type 			Nu, MPI, four-cylinder, DOHC

Capacity 		1999 cc (2.0-liters)

Bore x stroke 		81.0 x 97.0 mm

Power 			152 ps (112 kW) @ 6500 rpm

Torque 		194 Nm (19.8 kgm) @ 4800 rpm

Compression ratio	10.3:1

Fuelling 		Multi-point injection, 16 valves

Emissions rating 	Euro 2-to-5 depending on market

1.6-litre 134 ps

Type 			Gamma, GDI, four-cylinder, DOHC

Capacity 		1591 cc (1.6-liters)

Bore x stroke 		77.0 x 85.4 mm

Power 			134 ps (98.0 kW) @ 6300 rpm

Torque 		162 Nm (16.6 kgm) @ 4850 rpm

Compression ratio	11.0:1

Fuelling 		Direct injection, 16 valves

Emissions rating 	Euro 3

Diesel

1.7-litre 136 ps

Type 			U2, VGT, four-cylinder, DOHC

Capacity 		1685 cc (1.7-liters)

Bore x stroke 		77.2 x 90.0 mm

Power 			136 ps (100 kW) @ 4000 rpm

Torque 		330 Nm (33.7 kgm) @ 1750-2500 rpm [manual]

320 Nm (32.6 kgm) @ 1750-2500 rpm [automatic]

Compression ratio	17.0:1

Fuelling 		CRDi common-rail, high pressure injection, 16 valves

Emissions rating 	Euro 3-to-5 depending on market

Transmissions

Gasoline 			Diesel

2.0 	 	1.6 	 	1.7

Manual 		6-sp 		6-sp 		6-sp

Automatic 		6-sp 		6-sp 		6-sp

Technical specifications / All-new Kia Carens

Gear Ratios 		Gasoline 					Diesel

2.0 MT / AT		1.6 MT / AT 		1.7 MT / AT

1 				3.769 / 4.212 		3.769 / 4.400 		3.615 / 4.639

2 				2.040 / 2.637 		2.045 / 2.726 		1.794 / 2.826

3 				1.294 / 1.800 		1.370 / 1.834 		1.542 / 1.841

4 				1.024 / 1.386 		1.036 / 1.392 		1.176 / 1.386

5 				0.860 / 1.000 		0.839 / 1.000 		0.974 / 1.000

6 				0.756 / 0.772 		0.729 / 0.774 		0.829 / 0.772

Rev 			3.583 / 3.385 		3.700 / 3.440 		3.731 / 3.385

Final Drive 		4.188 / 3.510 		4.563 / 3.957 		4.063* / 2.885

*2.955 – ratios 3-to-6

Suspension and damping

Front 	Fully independent subframe-mounted MacPherson struts, with coil springs and gas-filled shock absorbers. Anti-roll stabiliser bar.

Rear 	CTBA (coupled torsion beam axle), with coil springs and gas-filled shock absorbers.

Steering

Type 			MDPS motor-driven electric power steering, with Flex Steer option

Wheel turns		2.7 lock-to-lock

Turning circle 		11.0 meters

Brakes

Power 			Single 11.0-inch booster

Front 	 		300 x 28 mm ventilated discs

Rear 			284 x 10 mm solid discs

Assistance 		ABS with EBD

100-to-0 kph 		40.8 meters

Wheels and tyres

Standard	 	16 x 6.5 inch steel  		205 / 55 R16

Optional 	 	16 x 6.5 inch alloy* 		205 / 55 R16

17 x 7.0 inch alloy 		225 / 45 R17

18 x 7.5 inch alloy** 		225 / 45 R18

Spare 			Temporary 16-inch ‘spacesaver’ wheel/tire

*standard on EX models, **EX models only

Note: 18" alloy wheel is not available with Gamma 1.6 GDI engine

Dimensions (mm)

Exterior

Overall length		4525

Overall width		1805  (excluding door mirrors)

Overall height		1610  (excluding roof rails)

Wheelbase 		2750

Front track 		1563-1573 (depending on wheel/tire combination)

Rear track 		1576-1586 (depending on wheel/tire combination)

Front overhang	  940

Rear overhang	  835

Ground clearance 	  151

Aerodynamics 	 0.30 Cd

Technical Specifications / All-new Kia Carens

Dimensions (mm)

Interior 		Front 		2nd row 	3rd row

Head room		1035 		1002 		867

Leg room 		1034 		  940 		707

Shoulder room	1438 		1440 		1313

Capacities (liters)

Fuel tank		58.0

Luggage (SAE)  	103 		behind 3rd row seats, to window

492 		behind 2nd row seats, to window (7-seater)

536 		behind 2nd row seats, to window (5-seater)

1667 		behind front row seats, to roof

Longest object 	2,150 mm 	can be carred with front passenger seat folded flat

Max roof load 		100 kg

Max towing capacity 	730-750 kg (unbraked trailer, depending on model)

1300-1500 kg (braked trailer, depending on model)

Gasoline 					Diesel

2.0 MT / AT		1.6 MT / AT 		1.7 MT / AT

Weights  (5-seater)

Curb weight (kg) 	1429 / 1452 		1394 / 1429 		1498 / 1517

Gross weight (kg) 	2030 / 2050 		1990 / 2020 		2100 / 2100

Weights  (7-seater)

Curb weight (kg) 	1442 / 1464 		1409 / 1439 		1522 / 1530

Gross weight (kg) 	2180 / 2210 		2150 / 2150		2240 / 2240

Performance

Top speed (kph) 	200 / 194 		185 / 178 		191 / 186

0-to-100 kph (sec) 	9.9 / 11.2 		11.3 / 12.0 		10.4 / 12.0

Fuel Consumption and Emissions*

Liters / 100 km	*7.5 / *7.8		** / **			5.4 / 6.0

CO2 (g/km) 		*177 / *184 		** / ** 			144 / 159

*depending on individual markets

**to be confirmed

JANUARY 2013