New Holland Construction launches new generation wheeled excavator range

New Holland launches its new generation of wheeled excavators, the B Series PRO. The three new models, ranging from 15 to 19 tons, excel in high precision work with their brand new controls and stand out for being remarkably easy to operate and service. They offer a highly professional package that delivers high productivity and reliability at low operating costs:

- High productivity and lifting performance with exceptional power, speed and stability

- High precision with brand new, extensively tested controls

- Easy operation and exceptional comfort with new controls and rational cab layout

- Excellent serviceability and reliability with easy ground access and new diagnostics software

- Proven performance and reliability through extensive endurance testing

Fast, powerful and stable

The B Series PRO wheeled excavators run high performance, large displacement FPT engines that deliver high torque and power. This performance is matched by that of the 3-pump hydraulic system, which maximises swing performance with a dedicated swing pump so that no power is diverted from the other hydraulic functions, resulting in greater efficiency and fast cycles. In addition, the large displacement engine and 3-pump system result in less wear, increasing the machine’s reliability.

The arm, available in three lengths for each model, has been redesigned to provide exceptional breakout force, 5% higher than in previous models. The automatic power boost kicks in when more power is needed, increasing pressure up to 370 bar. The new design of the B Series PRO optimises weight distribution and minimises the offset of the undercarriage, resulting in exceptional stability and equally high lifting performance at the front and the rear. All these features combine to deliver an outstanding lifting performance on wheels.

The new heavy-duty ZF axles and transmission provide excellent traction and deliver a higher maximum travel speed of 35 kph, reducing travel time between jobsites. The heavy-duty axles and higher ground clearance also contribute to the B Series PRO’s reliability and durability.

Brand new controls for high precision and versatility

The electro-hydraulic system has been re-engineered and now relies on a single integrated CPU instead of the three controllers of the previous models, with new software developed to maximise the machine’s uptime and deliver clear diagnostics. The new system and software have successfully completed an extreme testing programme to optimise their performance and reliability.

The 3-pump system enables the operator to carry out simultaneous movements under every load. The proportional controls and new low-effort joysticks with longer stroke further add to the excellent control characteristics of the B Series PRO in tasks requiring particularly high precision, such as levelling.

The B Series PRO is a true multi-function master. The operator has a choice of working modes to match the requirements of their task. The adjustable swing speed enables them to adjust power and brake force according to the operation. For special applications, the swing brake mode is easily permanently engaged with a dedicated switch. When the highest precision is needed, the operator can activate the levelling mode on the left joystick. Managing the attachment’s flow and pressure is very easy and up to 12 settings can be memorised for later use. With the attachment management system, proportional control and wide variety of possible configurations, the B Series PRO is designed to work with every type of attachment, offering exceptional versatility.

Easy operation and comfort combined with versatility

The entire cab layout and control design have been developed with the operator in mind, to make the machine’s operation intuitive and comfortable. The new dashboard with LCD monitor and screen dedicated to the rear view camera puts the operator in full control of the machine’s status. The rational layout of the controls makes it very easy to operate the machine. For example, all travel controls – road mode, creep speed, gear shifting, axle lock – are grouped on a switch pad placed on the steering column. The slider function for the blade and stabilisers is on the right joysticks, together with the travel direction control. The working and simplified swing brake modes are easy to select.

The spacious cab with pneumatic heated seat and large glazed areas offers an extremely comfortable workstation with excellent all round visibility, further enhanced by the rear view camera. With the ROPS and FOPS protection and exceptional stability of the B Series PRO, the operator can work with confidence. The comfortable cab and intuitive controls mean that they can maintain high productivity during long hours with minimal fatigue.

Easy serviceability for maximum uptime and reliability

All the main service points are grouped and easily accessible at ground level, so that daily maintenance operations can be completed quickly and efficiently. The side-by-side radiator layout results in an extremely reliable cooling performance and makes it easier to clean them. A front net keeps dust away from the radiators, lengthening the interval between cleanings.

The easy serviceability, added to the particular care that has gone into the durability of key components, from the heavy-duty axles to bucket linkages and the new design features such as the electro hydraulic controls and the 3-pump hydraulic system, contribute to the exceptional reliability and durability of the B Series PRO wheeled excavators, as shown by the thousands of hours of endurance tests they have successfully completed.

B Series PRO Wheeled Excavators – New Models Fact Box:

WE150B PRO	WE170B PRO		WE190B PRO

Net power (ISO):		90 kW		105 kW			118 kW

Max hydraulic flow

main pumps:			280 l/mn	288 l/mn		288 l/mn

Separate swing pump:		70 l/mn		72 l/mn			101 l/m

Traction force:			86 kN		92 kN			112 kN

Max speed:			35 km/h		35 km/h			35 km/h

Bucket digging force:		99.5 kN		112 kN			136 kN

Arm digging force:		72.9 kN		73.8 kN			91 kN

Operating weight PL (wt blade):	15.6 t		17.2 t			18.6 t

Operating weight P2AL

(blade & stabilisers):	16.4 t		18.0 t			19.5 t

Visiting our website, you will be able to download texts and high-resolution image files and video related to this press release (jpg 300 dpi, CMYK): www.newholland-tools.com/press-kit

Turin, 9 November 2012

New Holland Construction is a global, full-line construction equipment brand, with a network of 800 dealers and more than 2,100 outlets in 100 countries. The company brings together the strength and resources of its worldwide commercial, industrial and finance organizations. Thanks to the experience of its foundation heritage brands, New Holland can proudly point to quality, technologically state-of-the-art products that are fully compliant with safety standards and environmental regulations. New Holland Construction is a brand of CNH Global N.V., a majority-owned subsidiary of Fiat Industrial S.p.A. (FI.MI). More information can be found on line at www.newholland.com.

Press Office

Released by:

TLC PR for ALARCON & HARRIS

Lynn Campbell

Tel: +44 151 227 4957

E-mail: lynn@tlcpr.co.uk