New Holland Construction launches new C Series Dozer at Bauma

New Holland introduces the new C Series dozers, extending the offering with an additional model at the low end of the range, which now offers three models ranging from 13 to 20 tons. Redesigned from the ground up, the new C Series makes a complete break from the previous generation to offer new features that will allow operators to work faster and save fuel:

- 10.5% fuel savings with SCR technology combined with 19% higher efficiency (lt/m3)

- 9% to 16% power back up

- Best-in-class drawbar pull with hydrostatic transmission and new layout for perfect cooling

- High precision work with excellent visibility and controllability, and integration with GPS and laser guidance

- Quietest cab in the industry with just 76dBA

- Advanced Track Life tracks for abrasive conditions last twice as long as standard lubricated tracks

More performance and savings with state-of-the-art engine technology

The three models of the new C Series and feature New Holland’s well proven SCR technology, which brings a remarkable 10.5% fuel saving compared to the previous generation, based on hourly fuel consumption. The 6.7 litre FPT Industrial engine delivers an impressive incremental power of 9% for the D125C and D180C and 16% for the D150C. As a result, the engine is more reactive to load changes and the torque growth is higher to avoid big engine rpm drops.  The combined effect of New Holland’s SCR technology and the performance delivered by the powerful engine can drive the new models’ efficiency up to an exceptional 19%.

The D150C and D180C feature a new “V-shaped” cooling package that increases the cooling surface for better efficiency and easier radiator cleaning. This solution, together with the hydraulic reversible fan, reduces the radiator cleaning intervals. It also cuts fuel consumption, as the oil flow is strictly linked to the cooling demand. The easy maintenance is further helped by the reversing intervals that can be set on the on-board computer or engaged manually.

Best-in-class drawbar pull and versatility with the hydrostatic transmission

The three C Series models now feature a hydrostatic transmission that delivers best-in-class drawbar pull of 213 kN for the D125C, 311 kN for the D150C and 372 kN for the D180C. The entire system has been redesigned with a new layout that ensures perfect cooling even in the hottest climate.  With the new layout the oil is delivered directly to radiators instead of the tank, which now operates as a reserve of cooled fluid to further improve performance (the Air-to-boil level has been increased by 8% from 460C to 500C).

The hydrostatic transmission ensures a constant power transfer under load and the tracks’ counter-rotation allows the machine to turn easily in tight spaces.

The reversing setting can be changed electronically, so that the operator can choose between soft, medium and aggressive reversing modes on the on-board computer, for greater comfort and productivity. With the exclusive Proportional Dozer Control (PDC) mode, once the operator sets the maximum allowed speed, he can move the joystick forward or backward to increase or reduce speed continuously, achieving greater accuracy in fine grading applications.

Electronics at the service of precision

The new cab, which is 10 cm further forward than in the previous generation, provides perfect visibility on the blade and ensures better dozer balance. In addition to the excellent visibility, the new C Series offer the best controllability in the market. The new electrohydraulic joystick offers new features to deliver a perfect levelling performance and the complete integration with the most widespread GPS and laser guidance systems for high precision. The three models are available from the factory with a pre-installation kit for Topcon, Trimble and Leica electronic blade controls.

The new blade control joystick features several automatic functions, such as the “shaking mode” that automatically shakes the blade for faster cleaning and the “grading mode” that when engaged reduces blade speed by 50% for more accurate operation or enables the GPS control when one is installed. The blade reaction also has three possible settings, similarly to the hydrostatic transmission: soft for fine levelling, medium for most applications, and fast for heavy dozing when it’s needed to prevent the engine from stalling.

The blade control and hydrostatic functions are easily engaged with two buttons close together on the dashboard, so there are no levers that can get in the way of cab accessibility.

Operator comfort is enhanced by the quietest cab in the industry, with just 76dBA inside the cab.

Powerful pull with the strong structure

The chassis has been redesigned to enhance reliability and provide better accessibility to components. The blade cylinder geometry has been optimised to deliver faster reaction and higher pushing force. The new box section design of the PAT frame is exceptionally strong and prevents twisting when working with the blade at an angle. In Bulldozer configuration, the patented “Equistatic” device distributes the effort equally on the two push beams independently of the blade’s tilting, so that the wear of the frame and related components is reduced.

ATL tracks for abrasive conditions

When working in abrasive conditions, the exclusive Advanced Track Life (ATL) tracks provide the solution and they last twice as long as standard lubricated tracks. The system consists of two coaxial bushes where the external one is free to rotate when in contact with the sprocket, drastically reducing wear caused by friction. The sprocket has been modified with fewer teeth but with 40% more material under the tooth root area that triples the wear material between the teeth.

Maintenance has never been so easy

The new frame design minimises the time needed for the daily checks. All the main service points are within easy reach and the greasing points are grouped. Three belly plates are located on the lower part of the machine and a fourth wide one in the rear for oil replacement or extraordinary transmission work. The transmission can be reached from the cab through a dedicated door. All the hydraulic pressure, filters and electric components checks can be carried out from the ground simply by opening the cab’s two lateral hoods.

The undercarriage covers have been designed with a 49 degree angle to improve the self-cleaning effect when working in muddy conditions, reducing maintenance time for periodical machine cleaning.

More versatility with new options

New options such as the three-shank ripper, dedicated protection and winches for forestry applications, or front and rear tow hooks for standard applications.

C Series Dozers – New Models Fact Box:

D125C			D150C			D180C

Max power:	100 kW / 134 hp		121 kW / 162 hp		169 kW / 226 hp

Operating weight:	13 ton			16 ton			20 ton

Drawbar pull:	213 kN			311 kN			372 kN

Undercarriage:	LT / WT / LGP		XLT / WT / LGP		LT / XLT / WT / LGP

Blade:		PAT 			PAT / Foldable PAT /	PAT / Foldable PAT /

Bulldozer (XLT only)	Bulldozer

Turin, 15 April 2013

Visiting our website, you will be able to download texts, high-resolution image files and videos related to this press release (jpg 300 dpi, CMYK): www.newholland-tools.com/press-kit

New Holland Construction is a global, full-line construction equipment brand, with a network of 800 dealers and more than 2,100 outlets in 100 countries. The company brings together the strength and resources of its worldwide commercial, industrial and finance organizations. Thanks to the experience of its foundation heritage brands, New Holland can proudly point to quality, technologically state-of-the-art products that are fully compliant with safety standards and environmental regulations. New Holland Construction is a brand of CNH Global N.V., a majority-owned subsidiary of Fiat Industrial S.p.A. (FI.MI). More information can be found on line at www.newholland.com.

Press Office

Released by:

TLC PR for ALARCON & HARRIS

Lynn Campbell

Tel: +44 151 227 4957

E-mail: lynn@tlcpr.co.uk