26/07/2018

New Holland Intelligent Trailer Braking System delivers best-in-class safety and stability on T7 and T6 AutoCommand tractors

- Unique Intelligent Trailer Braking System

- Automatically controls the pneumatic brakes of trailed equipment

- Aligns tractor-trailer deceleration rates for improved stability

New Holland introduces a patented Intelligent Trailer Brake System onto its T7 AutoCommand™ and T6 AutoCommand™ tractors. This innovation, winner of an Agritechnica Silver Medal, enhances stability under deceleration with a trailer, particularly on low friction surfaces, resulting in greater safety for transport and field work. The system ensures that the deceleration rate of the tractor and its trailer are aligned when the driver reduces the tractor’s speed by using just the transmission, without applying the service brakes.

Typically when a tractor and trailer are slowed by just the transmission and engine braking alone the momentum of the trailer will push against the tractor. This pushing force can cause instability which may increase the potential risk of a jack knife situation, especially on steep gradients or low friction surfaces such as icy roads or grassland.

The Intelligent Trailer Braking System senses the reduction in the tractor’s speed and calculates the deceleration force using a torque sensor within the transmission. An electronically controlled trailer brake valve then automatically applies the trailer brakes to reduce the trailer’s speed at the same rate as the tractor. This automated braking prevents the tractor from being pushed by the trailer, greatly improving its stability and avoiding the risk of jack knifing. No modifications are required to the trailed equipment.

The controlled and harmonised braking force, between the tractor and the trailer,  delivered by the Intelligent Trailer Braking system also means that the stopping distance of the tractor and trailer is virtually the same as that of the tractor alone, even though the driver’s only input has been to reduce the speed using the transmission.

This new option compliments the list of brake features already available on New Holland tractors, including the award winning enhanced exhaust brake and ABS system, to deliver the most comprehensive brake package available in the Agricultural business.

New Holland Agriculture's reputation is built on the success of our customers, cash crop producers, livestock farmers, contractors, vineyards, or groundscare professionals. They can count on the widest offering of innovative products and services: a full line of equipment, from tractors to harvesting, material handling equipment, complemented by tailored financial services from a specialist in agriculture.  A highly professional global dealer network and New Holland’s commitment to excellence guarantees the ultimate customer experience for every customer. For more information on New Holland visit www.newholland.com

New Holland Agriculture is a brand of CNH Industrial N.V. (NYSE: CNHI /MI: CNHI) a global leader in the capital goods sector with established industrial experience, a wide range of products and a worldwide presence. More information about CNH Industrial can be found online at www.cnhindustrial.com

https://www.facebook.com/NHAgriUKandROI/

https://twitter.com/NHAG_UKandROI

https://www.instagram.com/NEWHOLLANDAG/

https://www.flickr.com/photos/newholland

https://plus.google.com/117086178528241801087

https://www.youtube.com/user/NewHollandAG

Press contacts:

Silvia Marcomini, Brand Communications UK&ROI - Phone: +44 (0) 01268 295 268

email: silvia.marcomini@cnhind.com