24/02/2019

New Holland introduces new features on CX combine range

- New Everest Sidehill Integral compensation system on CX7/8 and CR ensures super-sized productivity on steep in-field slopes

- New IntelliSteer-Lite™ automatic steering system for CX5 and CX6 delivers record-beating accuracy and return on investment

- New ECOBlue™ HI-eSCR 2 Stage V technology on CX8.80 and CX8.90 delivers clean performance and more power

New Holland Agriculture is introducing new features that will further help customers boost their productivity: the CX7/8 and CR are now able to deliver their super-sized productivity on steep in-field slopes with the new award-winning Everest Sidehill system, while the CX5 and CX6 benefit from the accuracy and efficiency achieved with the new IntelliSteer-Lite automatic steering system.

In addition to the new features, New Holland is introducing new engines featuring ECOBlue™                   Hi-eSCR2 technology for Stage V compliance on the CX8.80 and CX8.90. The highly fuel-efficient engines, combined with the new maintenance free after-treatment system, deliver a powerful performance with extremely low operating costs.

New Everest Sidehill Integral compensation system ensures super-sized productivity on steep in-field slopes

The CX7/8 and CR flagship combines are now available with the new, award-winning Everest Sidehill and Everest Integral compensation system. Models featuring this innovative system are engineered to counteract lateral slopes of up to 20% on all range.. Everest integral can counteract longitudinal slope up to 32% It keeps the threshing, separation and cleaning system perfectly level to offer high performance in side hills. The straw elevator entry section maintains optimal feeding on the steepest slopes. This, together with the level grain tank filling means that the combine’s performance is the same on the slope as it would be on ground level. The Everest Sidehill system can work in combination with a self-levelling cleaning shoe to deliver 100% efficiency on slopes of up to 30%.

The CX and CR combines featuring the Everest Sidehill system were awarded the “Machine of the Year” title at the SIMA 2017 for their benefits in terms of harvesting productivity and efficiency for customers who are working in challenging conditions. This innovative system was also recognised by the American Society of Agricultural and Biological Engineers with an AE50 award.

New IntelliSteer-Lite™ automatic steering system for CX5 and CX6 delivers record-breaking accuracy and return on investment

The CX5 and CX6 are now available with the new IntelliSteer-Lite™ factory fitted automatic steering system. It enables the operator to work at a higher forward speed, reducing the time needed to complete the job. The system’s accuracy also results in lower fuel consumption due to increased efficiency and less overlapping, maximising the customer’s return on investment. The operator benefits from lower levels of stress, as they can focus on the combine’s performance rather than steering. A further advantage of the new IntelliSteer-Lite system is that it can be moved to a tractor after the harvest season.

New ECOBlue™ HI-eSCR 2 Stage V technology on CX8.80 and CX8.90 delivers clean performance and more power

The CX8.80 and CX8.90 now comply with Stage V emissions standards, which mandate a further 40% reduction of Particulate Matter content compared to previous Stage IV regulation. They achieve the new emission limits with the NEF 6 and Cursor 9 engines and the new HI-eSCR2 technology developed by FPT Industrial. This innovative after-treatment system is a maintenance-free, patented solution that minimizes operating costs. The Cursor 9 engines feature a simple layout and are EGR-free, thus granting extreme productivity and reliability.

With the new Stage V set up, the flagship models at the top of the range become even more powerful, with the CX8.80 benefitting from a 14 hp increase in maximum power - to 305 kW (415 hp).

| MODEL | STRAW WALKERS | ENGINE | EMISSIONS | MAX. POWER kW/hp | Graintank litres |
| --- | --- | --- | --- | --- | --- |
| CX5.80 | 5 | NEF 6 | Tier 4B | 190/258 | 8,300 |
| CX5.90 | 5 | NEF 6 | Tier 4B | 230/313 | 8,300 |
| CX6.80 | 6 | NEF 6 | Tier 4B | 230/313 | 9,300 |
| CX6.90 | 6 | Cursor 9 | Tier 4B | 250/340 | 9,300 |
| CX7.80 | 5 | Cursor 9 | Tier 4B | 250/340 | 9,000 |
| CX7.90 | 5 | Cursor 9 | Tier 4B | 275/374 | 10,000 |
| CX8.70 | 6 | Cursor 9 | Tier 4B | 275/374 | 11,500 |
| CX8.80 | 6 | Cursor 9 | Stage V | 305/415 | 11,500 |
| CX8.90 | 6 | Cursor 9 | Stage V | 338/460 | 12,500 |

|  | Lateral correction | Longitudinal correction |
| --- | --- | --- |
| Everest | 20 % 37 % on cleaning shoe | / |
| Everest Integral | 20 % 37 % on cleaning shoe | 32 % uphill 10 % downhill |

New Holland Agriculture's reputation is built on the success of our customers, cash crop producers, livestock farmers, contractors, vineyards, or groundscare professionals. They can count on the widest offering of innovative products and services: a full line of equipment, from tractors to harvesting, material handling equipment, complemented by tailored financial services from a specialist in agriculture.  A highly professional global dealer network and New Holland’s commitment to excellence guarantees the ultimate customer experience for every customer. For more information on New Holland visit www.newholland.com

New Holland Agriculture is a brand of CNH Industrial N.V. (NYSE: CNHI /MI: CNHI) a global leader in the capital goods sector with established industrial experience, a wide range of products and a worldwide presence. More information about CNH Industrial can be found online at www.cnhindustrial.com

https://www.facebook.com/NHAgriUKandROI/

https://twitter.com/NHAG_UKandROI

https://www.instagram.com/NEWHOLLANDAG/

https://www.youtube.com/user/NewHollandAG

Press contacts:

Silvia Marcomini, Brand Communications UK&ROI - Phone: +44 (0) 01268 295 268

email: silvia.marcomini@cnhind.com