Press Release

The New SportContact 6 – High-Performance Handling, Grip, and Safety

- Super sports tire with new compound, tread technology, and structure

- Significant improvements in dry handling, steering precision, and high-speed suitability

- Continued rise in demand in 19–23 inch segment; approval expected from reputable vehicle manufacturers

Hanover, September 2015. Continental’s new SportContact 6 is a super sports tire for the high-performance segment that clearly improves on the handling, steering precision, and high-speed suitability of the previous model. To bring these improvements to the roads – with a performance boost of up to 14% in some cases – the technicians in Hanover have “reinvented” the chemical composition of the tread, the tread design, and the tire structure. From now on, 41 dimensions will be available for rims with diameters of 19 to 23 inches.

High-grip compound: “Black Chili” ensures optimum interaction with the road

To boost the performance of the new SportContact 6 even more, the chemists at Continental, the tire specialist, have further developed the “Black Chili” tread compound. In the new SportContact 6, two factors ensure optimum adhesion, even when pushed to the limits: The rubber compound is designed to mesh with the roughness of the road. At the same time, temporary atomic connections between the tire compound and the road surface ensure high adhesion, acting like small suction pads at nanoscopic level. Both factors make for the greatest possible adhesion in all directions – during braking, cornering, and acceleration and on both wet and dry roads.

Tread design: Supporting blocks for perfect handling

To achieve particularly precise handling and rapid steering performance, Continental’s tire designers use novel force vectoring technology for optimal force transfer. This technology deploys different tread elements on the inside, outside, and center of the tire. Depending on the size of the tire, three or four central ribs and the tire’s inner shoulder ensure maximum crosswise transfer of force, noticeably improving the direct translation of steering commands to the asphalt. Because the outside of the tire is subject to greater forces than the inside during cornering, the rib flanks are designed to be asymmetrical. This increases the stability of the ribs and allows greater forces to be transferred. When working on the outer shoulders, the tire designers combined the different block elements to form one larger unit. Large tread blocks on the outside are connected with interlaced elements in a second row of blocks. This allows the tread blocks to support each other during fast cornering and offer optimum lateral force transfer.

New Aralon 350 reinforcing material: Maximum safety up to 350 km/h

Continental’s new SportContact 6 is approved for up to 350 km/h. This means that not only does it need to offer perfect braking performance, handling, and directional stability, but its structure must also be adapted to these extreme speeds and the associated enormous centrifugal forces on the tire. To achieve this, Continental’s engineers have come up with an innovative structure that controls the huge forces on the tire, ensuring maximum driving safety. Here, they use the innovative “Aralon 350” material developed especially for the SportContact 6, a synthetic fiber in which two yarns made from strong aramid are closely interwoven with a yarn of flexible nylon. Implanted in rubber, this fiber is placed under the tread as a jointless cap ply. This complex structure acts like an additional steel belt and offers controlled, safe tire contour behavior even at speeds of up to 350 km/h.

Performance overview: Up to 14% development progress

With the new SportContact 6, Continental has once again made considerable progress compared with its already very good predecessor model, the ContiSportContact 5 P. Steering precision has been increased by 14%, while handling on dry roads has improved by 11%. The grip level when driving on race tracks has been increased by 4%, and the overall wet-grip characteristics of the new SportContact 6 are 2% above the high level of the previous model. In addition, service life and comfort have received a 7% boost.

First approval from vehicle manufacturer

With the new summer tire, Continental is continuing its successful range of high-performance tires. The new super sports tire is particularly suited to pure sports cars such as the Audi R8 or Porsche 911 as well as very sporty vehicles such as the BMW 5 Series or Mercedes AMG. The range also includes a suitable tire for the electrically powered Tesla S. Continental expects this market segment to become increasingly popular with customers and is anticipating annual market growth of just under 10% for the various sizes of the new SportContact 6. The new high-tech tire has already received its first seal of quality: Honda has approved the tire for the new Civic Type R before its official release and achieved a lap record on the Nordschleife at the Nürburgring. Further approvals from high-profile vehicle manufacturers are in the works.

Continental at the IAA 2015

At the IAA 2015, Continental is showcasing components for the car of the future at booth A 08 in hall 5.1. In addition to the new SportContact 6 super sports tire, a photo-realistic 3D cinema will be featured in which the dialog between a human and the vehicle as well as automated driving can be experienced. Under the tagline “Summer of Innovation”, visitors can find out more about new functions for greater safety, environmental protection, comfort and convenience. Our exhibit at the fair will be rounded off by a forum with numerous events on opportunities for future employees.

We look forward to seeing you there during the press days.

Continental AG
Continental develops intelligent technologies for transporting people and their goods. As a reliable partner, the international tire manufacturer, automotive supplier, and industrial partner provides sustainable, safe, comfortable, individual, and affordable solutions. In 2014, the corporation generated sales of approximately €34.5 billion with its five divisions, Tire, Chassis & Safety, Interior, Powertrain, and ContiTech. Continental currently employs approximately 205,000 people in 53 countries.

www.continental-corporation.de

Tire division
The Tire division currently has 24 production and development locations worldwide. The broad product range and continuous investments in R&D make a major contribution to cost-effective and ecologically efficient mobility. As one of the world’s leading tire manufacturers, with more than 47,000 employees, the Tire division achieved sales of €9.8 billion in 2014.

Passenger Car and Light Truck Tires
Continental is one of Europe’s leading passenger car and light truck tire manufacturers and is the world’s fourth-largest passenger car and light truck tire manufacturer in the original equipment and replacement business sectors. Product development for the Continental premium brand focuses on optimizing all safety-related features while at the same time minimizing rolling resistance.
www.continental-reifen.de

Media database
www.mediacenter.continental-corporation.com

| Contact: Alexander Bahlmann Head of PR, Passenger/Light Truck Tires Continental AG Tire Division Büttnerstraße 25, 30165 Hanover, Germany Ph.: +49 (0) 511 938 2615 Fax: +49 (0) 511 938 2455 alexander.bahlmann@conti.de www.continental-reifen.de | Klaus Engelhart Press Spokesman Passenger Car and Light Truck/Two-Wheel Tires Germany/Austria/Switzerland Continental AG Tire Division Büttnerstraße 25, 30165 Hanover, Germany Ph.: +49 (0) 511 938 2285 Fax: +49 (0) 511 938 2455 klaus.engelhart@conti.de www.taraxagum.de |
| --- | --- |