Transcription template for contents

| Original Language | Translation |
| --- | --- |
| A CNG car as seen from the inside |  |
| 1. TWO FILLER NECKS BENEATH ONE FUEL DOOR |  |
| The filler necks of both fuels (CNG and petrol) are integrated beneath a single fuel door, making them easy to use. It takes almost the same amount of time to fill up with CNG or petrol. |  |
| 2. WHAT ARE THE GAS TANKS LIKE? |  |
| They’re made of high resistance steel with an anticorrosion treatment. They reach a maximum pressure of 200 bars. |  |
| The gas is hermetically sealed in thanks to a set of solenoid safety valves that only open when the ignition is turned on. |  |
| A thermal fuse would melt and release the gas in a constant controlled manner in an extreme situation. |  |
| 3. GAS LINES |  |
| For maximum safety, the gas flows through the high pressure system via stainless steel tubes. |  |
| 4. PRESSURE REGULATOR |  |
| It reduces the gas pressure down from 200 bars to between 5 and 9, depending on driving and engine conditions at all times. |  |
| Pressure is regulated in two stages and controlled electronically. |  |
| 5. ENGINE |  |
| CNG Vehicles are equipped with an internal combustion engine that has been specifically developed to operate with natural gas. |  |
| The engine operates with gas by default and can be driven without switching over to the petrol tank. |  |
| When the gas supply is depleted, the system automatically switches over to petrol and the driver notices no difference. |  |
| 6. INDICATOR ON THE INSTRUMENT PANEL |  |
| Displays that the car is running on natural gas. |  |
| Two indicators display the levels of both fuel systems. |  |

Please, remember to:

- Translate everything inside the column on the left and keep the style provided including bold letters, and also capital/small letters in the corresponding words unless the rules in your language indicate another format.

- Double check the translation to make sure this is the information you need on the video: otherwise we run the risk of making mistakes and having to correct the video as well.

- Contact us if you have any doubt about the text or ask for the original video if it has not been yet provided.