Press Information

New drivelines from Volvo increase power and decrease fuel consumption

In January Volvo Trucks launched the world’s most powerful truck, with a power output of 700 hp. Now the company is renewing its entire driveline range. The result is higher power, up to three percent lower fuel consumption and significantly lower emissions.

“We work continuously to offer products that increase our customers’ income-earning ability and reduce their costs,” says Ricard Fritz, head of strategic planning at Volvo Trucks. “Our new drivelines with powerful, economical and reliable engines, Volvo I-Shift and the VEB+ engine brake allow the driver to maintain a higher average speed and to get more done in a shorter period of time. At the same time, fuel consumption is considerably lower.”

The renewal programme covers all variants of Volvo Trucks’ 7-, 11- and 13-litre engines, which are now available in Euro 5 configuration. A number of technical improvements with the focus on optimised combustion and a new SCR catalytic converter have made it possible to combine increased power with decreased emissions and lower fuel consumption. For the 11- and 13-litre engines, idling is now 2 dB quieter, a significant reduction. What is more, Volvo’s successful I-Shift gearchanging system has been further developed and features a range of new functions that contribute to lower fuel consumption and higher driving comfort.

Up to three percent lower fuel consumption

For a driveline consisting of Volvo’s 13-litre engine combined with I-Shift, fuel consumption can be lowered by up to three percent compared with the model’s predecessor (Euro 5 incentive).

“We took a leading position in fuel efficiency with our first generation of the 13-litre engine,” says Ricard Fritz. “With this new engine generation, we have strengthened our position still further.”

From 240 to 700 hp
The new engines offer not just low fuel consumption but also higher power output and torque. All told, Volvo Trucks’ engine range now encompasses power outputs from 240 to 700 hp.

13-litre engine with 540 hp and 2600 Nm

The Volvo D13, which can be specified on the Volvo FH and Volvo FM, is now available with up to 540 hp, an increase of 20 hp compared with its predecessor. Maximum torque has risen by 100 Nm to 2600 Nm and this is reached from just 1000 r/min. This gives the engine a broader operational range than before and it is now smoother and more responsive. Together with the increased torque, this results in fewer gearchanges and lower fuel consumption.

Approved according to Euro 5, tailored for EEV

The Volvo D13 and Volvo D11 are available in both Euro 5 guise and in versions that meet the even lower particle and smoke emission levels specified in the EEV (Enhanced Environmentally friendly Vehicle) norm. EEV is a voluntary framework that can be applied by local authorities to speed up the introduction of vehicles with a smaller environmental imprint.

“In many parts of Europe, truck owners are being encouraged to switch to vehicles that meet EEV,” says Ricard Fritz. “For this reason we are now offering both the Volvo D13 and the Volvo D11 in EEV versions.”

Volvo D11: wider range and more economical

As recently as last summer, Volvo Trucks launched a new 11-litre engine for the Volvo FM. The focus then was on weight-sensitive applications such as tanker and bulk haulage duties. Now the range is being broadened with more power outputs to make the Volvo D11 an even stronger alternative for regional transports, construction duties and refuse handling. The Volvo D11 is available in power outputs from 330 to 450 hp and has become a couple of percent more economical than the previous Euro 5 version.

“The Volvo D11 in combination with I-Shift and VEB also offers class-leading performance and fuel consumption,” says Ricard Fritz.

More power output variants for the Volvo D7

The Volvo D7, which is found in the medium Volvo FL and Volvo FE trucks, is now also available in additional power output classes.

“A wider range of power outputs means it is easier to optimise each truck for its application. And with up to 340 hp the Volvo FE is now an excellent alternative not just for regional distribution but also for more demanding construction duties and refuse operations,” explains Ricard Fritz.

New features in Volvo I-Shift

More than half of all Volvo FH and Volvo FM trucks are now sold with I-Shift and this proportion is increasing all the time. With the new version of I-Shift, the driver has access to more intelligent software functions that save fuel and improve comfort. It features a further-developed freewheel function, more scope for choosing fuel-saving gearchanges when driving without a load, and the possibility of driving on the idling regulator and avoiding unnecessary downchanges. It is easy to adjust speed when driving in traffic tailbacks, for instance. For construction and timber haulage duties, I-Shift is available with a new function that improves traction on poor and slippery surfaces.

Facts about Volvo Trucks’ new engine range

Volvo D13C – Euro 5

380, 420, 460, 500 hp for Volvo FM.

420, 460, 500, 540 hp for Volvo FH.

SCR exhaust treatment.

Max torque 1900 – 2600 Nm.

VEB max output 300 kW at 2300 r/min (option for 380 and 420 hp).

VEB+ max output 375 kW at 2300 r/min (option for all power outputs).

Power take-off max output 1000 Nm at a standstill, 650 Nm while on the move.

Oil change interval 100,000 km with VDS4.

Volvo D13C – EEV

420, 460, 500 hp for Volvo FM och Volvo FH.

SCR exhaust treatment.

Max torque 2100 – 2500 Nm

VEB max output 300 kW at 2300 r/min (option for 420 hp).

VEB+ max output 375 kW at 2300 r/min (option for all power outputs).

Power take-off max output 1000 Nm at a standstill, 650 Nm while on the move.

Oil change interval 100,000 km with VDS4.

Volvo D11C – Euro 5

330, 370, 410, 450 hp for Volvo FM.

SCR exhaust treatment.

Max torque 1600 - 2150 Nm.

VEB max output 290 kW at 2400 r/min (option for all power outputs).

Power take-off max output 1000 Nm at a standstill, 650 Nm while on the move.

Oil change interval 100,000 km with VDS4.

Volvo D11C – EEV

330, 370, 410 hp for Volvo FM.

SCR exhaust treatment.

Max torque 1600 – 1950 Nm.

VEB max output 290 kW at 2400 r/min (option for all power outputs).

Power take-off max output 1000 Nm at a standstill, 650 Nm while on the move.

Oil change interval 100,000 km with VDS4.

Volvo D7F – Euro 5

240, 260, 290 hp for Volvo FL.

240, 260, 300, 340 hp for Volvo FE.

SCR exhaust treatment.

Max torque 940 – 1300 Nm.

Engine brake with max output 188 kW at 2800 r/min (option for all power outputs).

Power take-off max output 600 Nm.

Oil change interval 100,000 km with VDS 3 or 4.

Volvo I-Shift

Automated gearchanging system with 12 forward gears and 4 reverse gears. Available with a range of alternative programs for optimal gearchanging in different application areas: Basic, Distribution & Construction, Long Haul & Fuel Economy, Heavy GCW Control.

Rear axles

New ratio alternatives for Volvo’s hub-reduction axles contribute to optimised fuel consumption.

For further information, please contact:

Per Nilsson, phone +46 31 323 33 49, e-mail per.nilsson.pr@volvo.com

Visit http://www.thenewsmarket.com/volvogroup to access broadcast-standard video from the Volvo Group. You can review and request video material, and choose to receive it as an MPEG2 file or on Beta SP tape. Registration and video are free to the media.

Volvo Trucks provides complete transport solutions for professional and business-driven customers. The company offers a full range of medium to heavy duty trucks, with a strong global network of 3,000 service points in more than 130 countries. In 2007 Volvo Trucks sold more than 100,000 trucks worldwide. Volvo Trucks is a part of the Volvo Group, one of the world’s leading manufacturers of trucks, buses and construction equipment, drive systems for marine and industrial applications, aerospace components and services. The Group also provides solutions for financing and service.