3.  KIA CEE’D ISG

Kia brings ‘Idle Stop & Go’ technology to the European market

Full scale production of the six new Kia cee’d ISG (Idle Stop & Go) models, which offer up to 15% fuel savings in city driving, began in Slovakia during December 2008 and deliveries to customers across Europe are now underway.

Kia cee’d ISG cars are available with a choice of 1.4-litre and 1.6-litre gasoline engines and each of the three cee’d family bodystyles – five-door hatchback, five-door sporty wagon and three-door pro_cee’d.  Three 1.4-litre ISG models are displayed at Geneva, with new tailgate badging.  Made in Europe, the ISG cars are the first Kia production models to benefit from the Korean Corporation’s continuing and massive investment in eco-friendly technologies for the future.

“The Kia cee’d has already established itself as a genuine rival to class-leading vehicles in the C-segment,” observes Mr Panu Vainamo, General Manager Marketing, Kia Motors Europe.  “Now, we are proud to rapidly transfer the ISG features from our ‘green-performance’ eco_cee’d concept car, shown at Geneva last year, to the Kia cee’d ISG production model which is exhibited this year and is now on sale in many countries.  This transfer boldly demonstrates Kia’s dynamic progress towards securing a greener future for personal transport.  With a CO2 rating from just 137 g/km, the ISG innovation will maintain the cee’d as a highly competitive challenger in its class.”

Kia’s innovative ISG system automatically switches the engine off when the car is stopped in traffic and restarts the engine instantly when the driver wishes to move off.  In typical city driving conditions, with heavy traffic and constant stop-start motoring, the ISG system dramatically cuts fuel consumption and emissions – by up to 15%.  In everyday mixed driving over town, country and motorway routes, the officially measured fuel saving is 6% on the combined cycle.

As part of the ISG system for cee’d, a new ‘smart’ starter motor is linked to an upgraded ECU, which monitors the car’s status at all times.  When the car comes to a stop, such as at traffic lights, the ECU uses information from various other control systems around the vehicle to decide if switching the engine off is appropriate.

A new ‘smart’ high-efficiency alternator suppresses electric power demand during acceleration and recharges the car’s battery during deceleration.  As a ‘fail-safe’ if the car’s battery power drops below 75% of maximum for any reason, or there is insufficient energy available for the next start-up, the system will abort its ‘Idle Stop & Go’ programme.

While the car is stationary, if the clutch pedal is depressed, the engine is instantly re-started – automatically – so there is no delay in setting off as the engine re-starting process is accomplished in the time it takes the driver to select first gear.

The new ISG-equipped Kia cee’d cars also benefit from a new-generation, lighter weight manual gearbox which more than offsets the small extra weight of the ISG system components.

Made in Europe, this new five-speed transmission weighs 5 kilos less than the previous unit and features a new selector mechanism.  Gear-changing forces are reduced, reverse is synchronized with fifth gear for easier selection and the overall ‘feel’ of the transmission is significantly improved.

Kia cee’d comparisons (hatchback gasoline models)

Engine 			CO2		L/100km	Overall Saving*	City Saving**

1.4 ISG			137 g/km 	5.7		6% 		15%

1.4 (standard)		145 g/km 	6.1		----- 		-----

1.6 ISG	 		143 g/km 	5.8		6% 		15%

1.6 (standard) 		152 g/km 	6.3		----- 		-----

*measured on the official ‘Combined Cycle’

**Kia Motors Corporation test data

Later during 2009, similar ISG technology will also be made available for the upgraded 1.6-litre diesel Kia cee’d and similar ISG technology will appear on other Kia models in years to come.

Ends