TECHNICAL SPECIFICATIONS

Kia Mohave

Body & Chassis

Five-door, seven-seater hatchback SUV, with all-steel body-on-frame-chassis construction.  Choice of two longitudinally-mounted gasoline engines driving all four wheels via a five-speed or six-speed automatic transmission (depending on model).

Gasoline Engines

3.8 V6 275 ps

Type 			Lambda V6

Type			Quad-overhead camshaft, six-cylinder, with CVVT and VIS

Capacity 		3.8-litres, 3778 cc

Max power 		274 ps (202 kW) @ 6000 rpm

Max torque 		36.9 kg.m (362 Nm) @ 4400 rpm

Valves			24 (4-per-cylinder)

4.6 V8 342 ps

Name 			Tau V8

Type 			Quad-overhead camshaft, eight-cylinder, with CVVT and VIS

Capacity 		4.6-litres, 4627 cc

Max power 		340 ps (250 kW) @ 6000 rpm

Max torque 		44.4 kg.m (438 Nm) @ 3500 rpm

Valves 		32 (4-per-cylinder)

Transmissions

3.8 V6	 	4.6 V8

Manual 		-----  		-----

Automatic 		5-sp 		6-sp

Gear Ratios

3.8 V6	 	4.6 V8

1 			3.827:1	4.171:1

2			2.368:1	2.340:1

3			1.520:1	1.521:1

4			1.000:1	1.143:1

5			0.834:1	0.867:1

6			-----		0.691:1

Reverse		2.613:1	3.403:1

Final Drive 		3.357:1	3.357:1

Suspension & Damping

Front 			Fully independent by Double Wishbones, with coil springs and gas-filled

shock absorbers. Anti-roll stabiliser bar.

Rear 	Fully independent by Multi-Link rear axle, with coil springs and gas-filled shock absorbers. Anti-roll stabiliser bar.  Automatic or manual control of self-levelling system.

Kia Mohave continued

Steering

Type 			Speed-sensitive hydraulic power-assisted rack and pinion

Gearing 		3.5 turns lock-to-lock

Turning Circle 		11.0 metres

Four-wheel drive Systems

1.  Part-Time 4WD

Electronically controlled single ratio (High) system delivers 100% of torque to rear wheels during normal road driving.  Manually selected 4WD mode splits torque 50/50% - front/rear wheels for enhanced stability during slippery conditions (up to 80 km/h).  Optional Rear LSD (limited-slip differential).

2.  Automatic Full-Time 4WD

Electronically controlled dual ratio (High and Low) system delivers 100% of torque to rear wheels during normal road driving and up to 50% to front wheels (automatically) during slippery conditions.  Low-ratio (for use up to 40 km/h) multiples engine torque by 2.4 times.  Optional Rear LSD (limited-slip differential).

Brakes

Power 			Single 9 x 9-inch booster

Front  	 		328 x 28 mm ventilated discs

Rear 			324 x 13 mm solid discs

ABS 			4-Channel anti-lock system with EBD

BAS			Boosts braking power during emergency stops

DBC 			Downhill brake control maintains 8 km/h speed during descents

HAC 			Hill-start assist control prevents slip-back on hill starts

Wheels & Tyres

Standard  		Alloy 17 x 7.5J with 245/70 R17 tyres

Optional 		Alloy 18 x 7.5J with 265/60 R18 tyres

Spare

Standard 		Full size (all models)

DIMENSIONS (mm)

Exterior

Overall length 		4880

Overall width 		1915 (excluding door mirrors)

Overall height 		1810 (including roof rails)

Wheelbase 		2895

Front track 		1630

Rear track 		1640

Front overhang	  875

Rear overhang 	1110

Ground clearance 	  217

Departure angle	  27.3 degrees

Approach angle 	  22.5 degrees

Kia Mohave continued

Interior

First 		Second 	Third (seat row)

Headroom 		1015		  990 		  965

Legroom 		1060 		  950		  835

Shoulder room 	1530		1500  		1415

Capacities

Fuel tank 		82.0 litres

Luggage (VDA) 	  350 litres  (all seats upright)

1045 litres  (with 50/50 split rear seatback folded)

2765 litres  (with 60/40 split middle seatback also folded)

Weights  [kg]

3.8 V6 		4.6 V8

Curb weight 		2051 		2124

Gross weight 		2720		2800

Performance

3.8 V6		4.6 V8

Top speed / kmh 	190* 		190*

0-to-100 kmh / sec 	 8.5 		 7.4

100-to-0 km/h		42.6        	42.6 metres

Towing (max) kg/lb 	2273 / 5000	3410 / 7500

Fuel Economy  (litres/100 km)

Overall			11.6		tbc

CO2 g/km 		276** 		tbc

*electronically limited / **estimated

-- Ends--