Embargoed: Not to be published before 11.30 CET, 4 March 2014

Kia unveils new seven-speed dual-clutch transmission

- Kia launches its first seven-speed dual-clutch transmission (DCT)

- Transmission will improve fuel efficiency and acceleration

- New DCT will appear on production models in 2015

Geneva, 4 March 2014 – Kia today unveiled its all-new seven-speed dual-clutch transmission (DCT) at the Geneva Motor Show, pointing the way for future transmission developments from the Korean brand.

The new transmission – the first of its type from Kia – has been engineered to balance greater fuel efficiency with improved performance and to deliver a sportier driving experience.

Designed as a more fuel efficient replacement for Kia’s existing six-speed automatic transmission, currently available as an option on the majority of Kia models, the new DCT combines the advantages of both manual and automatic transmissions while allowing for faster gear changes than both.

Throughout the development process, engineers have been targeting a seven percent improvement in fuel efficiency and a five percent improvement in acceleration (0-100 kph / 62 mph) over the existing six-speed DCT transmission.

NVH has also been a key focus for the team behind the DCT’s development, with an external damper ensuring a high level of refinement for the new transmission.

The DCT is made up of two dry clutches, each fitted with an electric motor-driven clutch actuator to improve fuel economy, and a pair of gear input shafts, one each for the odd and even gear ratios. This set-up enables the DCT to operate sequentially or to jump immediately to any of its seven forward gears (and reverse) depending on the driver’s requirements.

The continuous power delivery offered by the DCT minimises the loss of torque by the powertrain during gear shifting and ensures a smoother drive in all conditions. The wide ratio coverage afforded to the engine by the seven-speed gearbox results in improved fuel efficiency and performance over rival six-speed DCTs.

The new seven-speed dual-clutch transmission will start to appear on production Kia cars in 2015.

- Ends -

Editors’ Notes

Kia Motors Europe

Kia Motors Europe is the European sales, marketing, and service arm of Kia Motors Corporation. With its headquarters in Frankfurt, Germany, it covers 30 markets in Europe.

# About Kia Motors Corporation

Kia Motors Corporation (www.kia.com) – a maker of quality vehicles for the young-at-heart – was founded in 1944 and is Korea's oldest manufacturer of motor vehicles. Over 2.7 million Kia vehicles a year are produced in 10 manufacturing and assembly operations in five countries which are then sold and serviced through a network of distributors and dealers covering around 150 countries.

Kia today has over 48,000 employees worldwide and annual revenues of US$43 billion. It is the major sponsor of the Australian Open and an official automotive partner of FIFA – the governing body of the FIFA World Cup™. Kia Motors Corporation's brand slogan – "The Power to Surprise" – represents the company's global commitment to surprise the world by providing exciting and inspiring experiences that go beyond expectations.